March 24, 2002

To: 	John White, P.E., Project Engineer

Washington State Dept. of Transportation (WSDOT)

6431 Corson Ave S., MS 61,

Seattle, WA, 98108

whitejh@wsdot.wa.gov

Subject: Comments Submitted March 24 on SR509 Corridor Completion/I-5/South Access Road Project to the Dept of Transportation

Please contact me if you have any questions or require substantiating data. This submittal includes four electronic files in case size limitations on email are an issue.

arleneSR509commentsMar25.doc

arleneAtt C airhealth2001.ppt

arleneAtt D Corps Nov99.doc

arleneAtt E 3rdtry POSpermit.doc

Thank you for this opportunity to comment. I just hope this effort wasn’t a waste of my time or your time. Politics in Seattle seems to ignore physics, economics, engineering, topography and any regulation they don’t like.

Submitted by  Arlene Brown

239 SW 189 PL

Seattle WA 98166

Home (206) 431-8693

For your address book, use my permanent e-mail arlene@mail.alum.rpi.edu - forwards to my current ISP.

# Table of Contents

Table of Contents	2

Summary	3

Violates FAA Object Free Area (OFA) Rules	4

Encroaches on Runway Protection Zones	5

Violates FAA’s Object Clearing Criteria	5

2 to 1 slopes Ignore airplane vibration induced damage	6

Inability to protect airport with highway in runway protection zone	6

Grossly underestimated secondary and cumulative Impacts	6

Identify fill quantity, source and cost	7

Toxic Soil Handling and Mitigation required for Workers & Neighborhood	8

Admit to total Destruction of Des Moines Creek	8

Neglects to mention it reduces available drinking water forever	9

Clean Air Act Analysis Assumptions Based on Ancient Inaccurate Analysis	9

Base Buy-out Area on Life Expectancy Reduction Calculations	13

Mitigation should include health monitoring and new play fields	13

Need cumulative noise impacts from airport and increased highway traffic	14

Construct noise barrier for S 196th Manmade Noise Amplifier Canyon	15

Eliminate or mitigate the 150 foot plus high Giant Noise reflector	15

Attached Public Hearing Comments address more issues	16

New earthquake hazard information	16

First Ave road failure when 3 to 1 slope not used	16

Best Management Practices already shown to be insufficient for this location	16

Archeological information not included in SR509 EIS	16

Procedural and Administrative Comments	16

Closing	17

Attachment A: Incomplete copy submitted at Public Hearing	17

3) Comments applicable to all project	20

Attachment B: Airport Pollution and Health	23

Airport Pollution Rankings and NY Asthma data	23

Ozone Nonattainment for the top 50  airports	24

NRDC Toxic Air Pollution Map	24

Attachment C: King County Health Data	26

Attachment D: Partial copy of Nov 1999 Health, Air, Soil Comments to Corps	26

Attachment E: Partial copy of Feb 2001 Health, Air, Soil Comments to Corps	26

Attachment F: References and Bibliography (Partial List)	27

References using letters	27

Additional References (note changes to numbers)	31

# Summary

Section 3.17, “Secondary and Cumulative Impacts” so understates the situation, it borders on fraud. The omissions and inaccuracies I do not believe are intentional on the part of the DOT but rather due to insufficient information being provided by the Port of Seattle and their representatives. Steps need to be taken to avoid Clean Air Act violations and premature death from excessive noise and air pollution.

If regulations are enforced and best management practices implemented, it will be cost prohibitive for the SR 509 extension/South Access Road project and the Sea-Tac third runway project to co-exist. The cumulative impacts on the wetlands, creeks, aquifer, noise, air pollution, salmon, Puget Sound resident orca pod, bald eagles and people are so great they are unimaginable. These impacts result in more flooding, more earthquake damage, more illness, more deaths and less drinking water. Ultimately, it will lead to Clean Air Act non-compliance whose costs will fall on King County’s business community.

Site Seismicity beginning on RDEIS Chapter 3, Page 3-55 needs a major overhaul to include the data collected since 1985 such as the February 2001 quake information and the SHIPS program data (see Attachment A). A geological survey is needed that specifically looks for soft soils. In addition, the interaction of the 3rd runway’s record-breaking wall with soft soil,s and the amount of damage that will cause to SR509 overpasses and roads in an earthquake, needs to be calculated.

Ignoring the intent of the FAA’s Runway Protection Zone rules is questionable. However, the clear violation of the FAA’s Object Free Area rules is so serious that the project should not proceed without written permission from the FAA that is accompanied by a risk analysis. The State’s lawyers may also want to review the rules to determine legal liability in the even of a lawsuit.

Even in the absence of the third runway, the mitigation for this project needs to more than normal because the area is already so unhealthy due to the airport and has unique characteristics such as high ongoing vibration exposure. A much larger buy-out area, more noise barriers, more gradual slopes, and a plan to ensure a steady supply of uncontaminated drinking water, etc. is needed.

It is obvious reading through this document that it has not had the level of engineering scrutiny this would have had if the Cities or any major citizens groups were against this project. Although I too support the concept of extending the “highway to nowhere” for the sake of King County, as currently written it underestimates hazards, provides inadequate mitigation and does not offer reasonable assurance of compliance with environmental or FAA regulations.  It’s UNSAFE.

# Violates FAA Object Free Area (OFA) Rules

FAA Advisory Circulars are considered mandatory in order to be eligible for Federal funding. Paragraph 307 of FAA Advisory Circular Airport Design AC150/ 5300-13 states “Objects non-essential for air navigation or aircraft ground maneuvering purposes are not to be placed in the OFA. This includes parked airplanes and agricultural operations. Tables 3-1, 3-2 and 3-3 specify the standard dimensions of the runway OFA. Extension of the OFA beyond the standard length to the maximum extent feasible is encouraged. See Figure 2-3.” (electronic page 33 of web http://www.faa.gov/arp/pdf/5300-131.pdf version). Para 212 a (2) expressly forbids automobile parking lots in the OFA.

For the long runway at Sea-Tac, the Object Free Area (OFA) extends 1000 feet from the runway end and is 800 feet wide (It’s a rectangle within the trapezoidal RPZ). The highway goes right through the object free area for this runway. Is the plan to discontinue flying large jets out of Sea-Tac so the OFA will be shorter or have you arranged for the FAA to ignore their own safety rules? If it’s unsafe for parked aircraft, potatoes, or parked cars, why is it safe for commuters in vehicles that contain fuel? Has this exception to the rules been approved by the FAA?  If an accident occurs will the victims sue Washington State and the FAA for damages?

Will de-icer that rots the stomach of fish when present in only parts per billion fall onto moving vehicles and be spread further than it is already? (De-icer has very deadly proprietary ingredients in it. It is not just harmless glycol as some assume.)

Will the frozen contaminated toilet chemical crystals that fall from leaky aircraft toilets land on vehicles and spread their germs even farther than currently? They contain viruses that our sewer treatment plants are not strong enough to treat.

# Encroaches on Runway Protection Zones

FAA Advisory Circular (AC) for Airport Design, AC150/ 5300-13, Change 4, Table 2-4, Figure 2-3 and Figure 2-4 defines the Runway Protection zone dimensions (http://www.faa.gov/arp/pdf/5300-131.pdf).  The AC defines the Runway Protection Zone (RPZ) as “An area off the runway end to enhance the protection of people and property on the ground”  (page 15 of pdf version). Section 212 provides more information such as expressly forbidding a church, mall or a golf club house but does permit a golf course.

There can be a little more latitude with the area of the RPZ’s that is outside the OFA area when the airport does not own the property and is unable to buy the property. However, in this situation it would be difficult to justify the exception. particularly since fuel storage facilities are strictly forbidden in the RPZ. Busy highways are a continuous conveyor belt of fuel.

# Violates FAA’s Object Clearing Criteria

Item 8 of Para 211, Object Clearing Criteria of AC150/ 5300 states:

“Other objects which require clearing are those that generally can have an adverse effect on the airport. These include objects in the inner part of the approach (coinciding with the RPZ) such as fuel handling and storage facilities, smoke and dust generating activities, misleading lights, and those which may create glare or attract wildlife.” (page 25 of pdf file).

Will the highway traffic lights interfere with landing and take-offs?

# 2 to 1 slopes Ignore airplane vibration induced damage

3 to 1 slopes are recommended for wetlands areas and are also part of the FAA building codes for reasons unrelated to wetlands. 3 to 1 slopes, or perhaps even less steep, are needed because the close proximity to the runway ends greatly increases the amount of vibration the construction, and then later the actual roads, will be subjected to. Close proximity is an understatement since the plan is to build where it’s expressly forbidden to build by FAA AC 150/5300.

To make matters even worse, we have a very active underwater ground water system that moves the earth: We are the highest portion of the large aquifer system and we have a large number of small earthquakes. These movements combined with the aircraft vibration all make this an unusually complex build site. Since aircraft at the airport vibrate the earth all the way into the heart of Normandy Park, can you imagine the amount of vibration the earth will feel in the Object Free Area! Flight paths have even been moved temporarily away from Magnolia during heavy rainstorms to avoid landslides.

One of the reasons the Port now faces building a record-breaking wall is because the EIS called for 2 to 1 slopes that the Army Corps of Engineering objected to. (I refer to it as a record- breaking wall since it’s only four tiers when you would expect it to be at least seven to even remotely resemble the few other tall MSE walls. More of Miller Creek would need to be moved and soft soils excavated over a large area if they wanted to build a safe MSE wall.)

# Inability to protect airport with highway in runway protection zone

The road going through the runway protection zones is inconsistent with FAA building criteria. It will be very easy to shoot at an aircraft and speed away on the highway.

# Grossly underestimated secondary and cumulative Impacts

The SR509/South Access Road plan induces growth contrary to the assumption in 3.17.1. It will induce so much air traffic and airport related ground traffic growth that ozone exceedences will occur unless measures are taken to cap pollution.

A cumulative pollution analysis of the proposed third runway and SR509 is essential to the SR509 project. So essential, that if done with sound engineering judgment, you will realize the two projects are completely and totally incompatible.  Combined they simply create too much impervious surface, too much air pollution, too much ground water pollution, it's too hard to control flooding, too much noise and greatly reduces the health and life expectancy of the residents. Since the Sea-Tac Master Plan Update never even did an environmental analysis on the impact of 1,500,000 haul trucks on Puget Sound region and did not have a record-breaking wall that would reflect noise, you can hardly think they would have really adequately addressed the SR 509 extension.  They said the analysis would be done as part of  THIS  plan.

The RDEIS plan also makes the “highway to nowhere” a preferred route for many commuters that completely bypass Burien currently. Other than an increase in airport haul truck traffic, there has not been a dramatic change in traffic on SR509 since 1979 when I first started using it regularly for the sections south of SW 128 St in Burien. SR 509 will forever dramatically alter Normandy Park and Burien.

# Identify fill quantity, source and cost

The SR509 EIS does not appear to identify the quantity of source of any fill needed for this project. The proposed Sea-Tac third runway will use up most of, if not all of western Washington’s supply of permitted fill making a huge fill shortage. Any fill needs must be addressed in the EIS.

You should not make the same mistake as the third runway that hoped they would be able to use a significant amount of the existing dirt. Contamination, peat bogs, wetlands, drinking water aquifer, federally protected wellhead and creek concerns make it difficult to use fill in the area.

Also available western Washington fill is likely to be toxic. The DOE is attempting to set the fill contamination criteria for the third runway to be equal to the state’s toxic clean up level, presumably due to the difficulties of finding clean fill. For instance, the third runway Clean Water permit that has had a “stay “ against it since fourth quarter 2001  allows lead at more than 10 times background level, arsenic at more than three times background level as well as toxic man-made chemicals not found naturally.

# Toxic Soil Handling and Mitigation required for Workers & Neighborhood

Before disturbing any soil, contamination tests need to be run because it is on top of an aquifer with fractured till and contamination is likely due to ASARCO and airport activities. Special handling techniques will be needed to address worker safety issues, public health issues as well as air pollution issues.

Recent DOE studies in conjunction with Seattle- King County Dept of Health have revealed unusually high metal contaminants in soils in Normandy Park and the surrounding area. For example, they had a lead reading of 490 compared to the clean up level of 250. Some of the toxics are attributed to ASARCO. The DOE only tested enough chemicals (arsenic, lead, antimony, bismuth and a couple of others) to confirm the area was in Asarco’s path, and did not identify the full extent of ASARCO chemicals that have polluted the area.

It is also known that there is contaminated soil on airport property from airport activities and that contamination was left behind when the Port of Seattle bought out properties.

Topography and winds are obviously a big factor so more tests are needed to determine the extent of pollution prior to construction so the proper mitigation measures can be taken.

# Admit to total Destruction of Des Moines Creek

The new South Access road to the airport is so close to the Des Moines Creek that it means either a slow or fast death to the creek and contamination of the aquifer that is only about 2 feet from the surface of the ground in that location. The plume of sediment toxics that surround highways are well known by the toxic sediment community. The creek will have to deal with pollution from the Highway plus the new airport road plus the airport. What other projects will impact that area? What happened to SASA?

# Neglects to mention it reduces available drinking water forever

DREIS section 3.5 on Groundwater is totally inadequate. The project permanently reduces the recharge to the aquifer and virtually guarantees the eventual contamination of the aquifer. This reduction in drinking water is even more painful when you realize the third runway also permanently reduces the recharge and increases contamination risks. There is already DOE documented jet fuel contamination in the aquifer so don’t respond to this comment with the Port’s song and dance that the aquifer layers aren’t connected.

What will we drink sixty years from now when the City of Seattle refuses to renew the current water agreement making the Highline aquifer a sole source aquifer instead of just supplying a portion of our water? A water shortage is being forecast even for rainy Seattle and it is expected to become our most precious resource in this century. A program should be set up by the state to pay the Highline Water District, the current going rate of water, in perpetuity, for the loss of the water from the combined projects regardless of whether it’s from reduced recharge or contamination or both. To ask us to give up our water for both a 3rd runway and a highway extension when we have already given up water for the existing airport and highway is just too much, particularly when a portions of the project virtually guarantees contamination.

This proposal  is somewhat similar to Seattle Water Dept’s request during the airport’s SEIS Master Plan Update process. However, when Borrow site 5 by the wellhead was eliminated as a fill source, they backed off on their request to indemnify the water.

# Clean Air Act Analysis Assumptions Based on Ancient Inaccurate Analysis

A complete air conformity analysis is needed to assess the pollution situation and identify mitigation measures.

A short description below indicates why the analysis needs to start from scratch rather than building on obsolete ones from the last century.

Start - Airport Master Plan Update Supplementary EIS 1997 –

Sea-Tac airport is "surface transportation limited",

Clean Air Act calculations therefore ASSUME NO additional aircraft with third runway or from other improvements. In other words, airport couldn't really grow - it was the assumption that helped them avoid triggering the Clean Air Act de minimus limit that would have required a formal air conformity analysis.

Add - new road to airport and SR 509 extension - all part of the current proposal so airport no longer surface transportation limited

Consequences (planned and unplanned depending on who you are)

- Additional 200,000 aircraft plus the additional surface transportation and ground equipment that goes with it

- Mixing of airport chemicals with the highway chemicals (highway to go through airport safety zone - (great place to shoot aircraft down by the way) making more hazardous combination of chemicals and turning things into ozone faster

- Abnormally high health risk for highway construction workers

- Abnormally high health risk for highway commuters if highway gridlocks like I-5

Net result

- The pollution they save with SR 509 is less than the NEW POLLUTION they get by actually being able to really increase Sea-Tac growth - OZONE Exceedences you can bet on from aircraft NOx that mixes with other chemicals and changes into ozone. SR 509 Project ADDS NOx and Ozone by increasing airport ground and surface traffic!!!!! The increased airport activity will create more than 300 tons of additional NOx per year.

- Impaired health of construction workers as a result of third runway construction pollution combined with airport activities

- Huge health risk for anyone sitting in traffic under the flight path

Near term Action

Perform cumulative air analysis. However, they really bizarre assumptions in the Sea-Tac Master Plan Update need to be corrected rather than incorporated into the analysis. Although some at the EPA suspected at the time the assumptions were invalid, there has now been enough data has been collected since that time to prove they were bizarre.  Issues that need to be corrected include:

- Construction schedule, designed specifically to avoid triggering limit, is no longer valid

- Applied pollution offsets from public road improvements and parking lot only to the third runway alternative even though the improvements would occur with either alternative

- Used bogus taxi times for third runway

- Used bogus delay savings that even airlines such as United subsequently objected to in writing to FAA referencing their own analyses showing a maximum savings of less than 30 seconds per aircraft.

- Fleet mix assumptions

- Emission parameters

- Overestimated third runway operations and underestimated third runway operations

- Did not account for additional operations technology such as gate software that eliminates gate monopolies allows.

Solution

- Kill 3rd runway so not as close to maximum airport chemicals. Bonus - the record wall on soft soils won't take out the highway in a quake

- Perform full up Clean Air Act conformity analyses using cumulative impacts including maximum airport growth. Ways to mitigate the problems analysis will reveal include:

  - Place permanent air monitoring station at airport - limit operations as needed (so we won't get as bad as Europe when they have had to shut down entire airport for a day things got so bad)

  - Limit number of operations at airport to avoid ozone exceedences down wind of airport (note the CO we save from the SR 509 is not our County's problem. It's NOx !!!!!)

  - Post highway signs saying to keep windows closed when under the flight path near the runway ends when in heavy traffic  (you can really smell unburned jet fuel when near the tunnel on the south end of the airport now but the traffic moves there so you aren't subject to it very long)

- Conduct health risk analyses and make a larger buy-out zone since the combined pollution of highway plus 3rd runway construction or 3rd runway operation creates a much higher risk - it is more than the sum of the parts. Note buy-out area is larger with third runway than without the third runway. But, even without the third runway, as long as they are on what should be airport property, I suspect the health analysis will indicate a larger buy-out area than planned. An expert one time referred to the airport area as a "toxic stew". His description really says it all.

- Make workers sign waivers recognizing the dangers so they can't sue. Set minimum health standards for workers - no high heart attack risks or major asthma problems or major cancer risks. Anyone being treated for cancer already should not be allowed to work under flight path for more than two days.

Please note the published DOE reports available on the web in recent years have some errors regarding ozone exceedences. Someone at DOE was nice enough to point this out to me. There are now some EPA databases on the web that I think are more accurate. However, I don't think they report the stations that do not operate 12 months a year that also had exceedences. Ozone is a real problem. The Port of Seattle likes to talk about CO since road improvements and parking lots have really cut that down around the airport. The Sea-Tac3rd runway analysis took credit for the public roads and new parking lot only in the 3rd runway scenario and so was able to avoid triggering the Clean Air Act diminimus limit that compares pollution levels (pretended 24 St would only exist if the third runway did).

Even dirty Texas is monitoring NOx at a major airport so my suggestions are not as "wishful thinking", as they may first seem. Europe wouldn't have closed airports on bad air days if airport pollution wasn't a real concern. We need to learn from Europe's mistakes and from California's solutions (stricter environmental laws than Federal because mountains trap pollutants). Boston is pursuing charging fees based on how much an aircraft pollutes like some places in Europe already do- a potential funding source for the air monitor?

# Base Buy-out Area on Life Expectancy Reduction Calculations

Considering recent high level court decisions, it is no longer enough to just focus on the pollutants that are monitored by the Clean Air Act (NOx, ozone, CO, etc), government is being forced to recognize and mitigate activities that expose people to pollutants that are known to impair health (Reference Hogue, Cheryl, Clean Air Act Faces Off Against Disabilities Act, Chemical & Engineering News, 11 September 2000. Page 6). Literally hundreds of reports in recent years have been released linking health problems to airport and surface traffic pollution. Since this proposal goes through runway protection zones, it mixes maximum airport pollutants with highway pollutants creating one of the worst environments known to man. A much larger buy-out area is needed than is customary for highways, particularly if the third runway wetlands permit are granted. If we had a 53 square mile buffer zone like the new Denver airport this might not be an issue but we have a postage stamp for an airport.

# Mitigation should include health monitoring and new play fields

The Washington Dept of Health studies done in conjunction with the Seattle-King County Health Dept already have identified a number of illnesses, some fatal, that are higher around the Sea-Tac. They tend to be those associated with pollutants. The three reports are at http://www.metrokc.gov/health/phnr/eapd/reports/cancer/. Since I was a Community Health representatives for this project, I have continued to read the new literature on the subject as it becomes available. It would take months to just summarize all of them. It turns out respiratory illness (asthma, cardiopulmonary disease etc) may be an even bigger issue than cancer. It’s a complex situation since King County is a sick county already so using it as a baseline is questionable.

Attachments C, D and E contain some additional information on this but its not even a drop in the bucket compared to what’s available on the web (or even on my computer’s hard drive for that matter). It’s really scary stuff. You can hide behind the problems with small population statistics only for so long.

A database needs to be set up to monitor the health of businesses and homes subjected to airport and highway pollution since this plan greatly increases the pollution for both. Highline School district should be required to monitor absences at the district level to identify trends to determine when airport operations need to be capped to compensate for the additional highway traffic. Lung capacity measurements should be added to the eye and ear exams. Asthma in children is a huge problem related to pollutants.

The SR509 extension/South Road access plan will greatly increase both the ground and air pollution at play fields near SR509. To make matters even worse, the third runway record-breaking wall will help trap pollution rather than absorb it like the mini-forest did. New fields, further away from the SR509 extension are needed for fields such as the North Elementary school field and Moshier field.

# Need cumulative noise impacts from airport and increased highway traffic

Airport populations, whose health is already impaired by airport pollution and sleep deprived from airport noise, are disturbed more readily by other noises such as increased highway noise. More highway noise mitigation is needed for highways built in close proximity to airport flight paths. Airport noise models do NOT take into account the effect of reflective surfaces and therefore vastly underestimate noise disturbances from increased impervious surface. A cumulative analysis is needed that includes impacts from reflecting surfaces that replace sound absorbing shrubs and trees. Health studies have shown too much noise can literally turn serious illnesses into terminal illnesses (the straw that broke the camels back).

# Construct noise barrier for S 196th Manmade Noise Amplifier Canyon

Recent destruction of mini-forests and the replacement of them with giant warehouse complexes and fenced housing developments have created a manmade cavern that seems to amplify airplane noise as it travels west towards the sound along S196 St. Homes that never heard airplanes prior to the construction of the manmade canyon, are now subjected to noise in at least the 70 db Level. The proposed highway cuts across this street in such as way that it will add to the already unbearable noise. The manmade canyon directs pollutants to the west subjecting residents to additional air pollution. The mixing of hazardous airport pollutants with hazardous highway pollutants will make it one of the most hazardous places in King County to live.

# Eliminate or mitigate the 150 foot plus high Giant Noise reflector

If a 150 high hard surface wall with 20 feet of fill on top of it is placed along the west side of SR 509 near S160 St to hold back the enormous quantities of third runway fill, it will be a giant noise reflector. The highway currently is underutilized so noise is more an issue if the SR509 extension is built which will greatly increase traffic. The wall did not exist during the Sea-Tac Master Plan Update EIS time frame. At that time it was to be a sloped hill that would have not have been like a giant reflector. The newer wall on the north end of the airport noticeably increased noise when it was built and the record-breaking wall will be much worse.

The great wall will reflect the additional highway noise into the communities to the west of the highway will be cost prohibitive to mitigate. Therefore, thhe third runway needs to be killed in order for the highway changes to proceed. The bare hill that has replaced the min-forest already reflects highway noise into the heart of Normandy Park, as well as Burien, where there was no noise before the 3rd runway construction started. A RDEIS section 3.17 assumption that environmental analyses would, or have been done, was incorrect.

The third runway proposal actually now has more than just the one record-breaking MSE wall so noise impacts from all the walls should be assessed.

# Attached Public Hearing Comments address more issues

Attachment A contains comments on a variety of subjects including more information on topics preceding this section as well as, but not limited to:

## New earthquake hazard information

## First Ave road failure when 3 to 1 slope not used

## Best Management Practices already shown to be insufficient for this location

## Archeological information not included in SR509 EIS

# Procedural and Administrative Comments

The soft soil maps need to be improved.

It’s too hard to identify proximity of creeks.

The web based RDEIS was greatly appreciated especially since the libraries that supposedly had a hard copy either didn’t  (or if they did, they don’t know it). The maps were easy to use on the web. The CD was also appreciated since it was easier to use than the online version for reading text.

Most people do not know about the South Access Road part of this proposal. Neither the newspaper meeting notices or the news coverage made it clear that there was a new road. If it weren’t for the great map in the newsletter sent out this year, I would not have realized it.

Last year’s Tyee public meeting was held at the busiest time of the year for public meetings related to the expansion of Sea-Tac Airport (Army Corps and Noise hearings with submittal of public comment all within few weeks of each other). Likewise, this year it fell in the same time frame as a noise hearing and the two weeks of Pollution Control Board meetings.  It feels as if the government agencies are ganging up on us and putting all the meetings within a one-month period so we have to pick and chose what meetings to attend. I suspect, just like last year, when we look back next year at the time period of your 2002 meetings and comment period, February thru March will correspond with the peak anti-runway meeting time frame for the entire year.

# Closing

Unfortunately, due to time constraints I cannot address all issues or identify all my specific references in the text so I have enclosed a partial reference list. I made an effort to bold the most relevant.  The references starting at 117 from the Journal of Geotechnical and Geoenvironmental Engineering are particularly relevant to the 3rd runway wall and its impact on SR509 in an earthquake.

Feel free to contact me if you want me to identify the source(s) of information that was provided verbally at the Feb 27 hearing or herein.

# Attachment A: Incomplete copy submitted at Public Hearing

Feb 27, 2002                           (does not include soft soil and earthquake fault maps etc)

To:

John White, P.E., Project Engineer,

WSDOT, 6431 Corson Ave S., MS 61, Seattle, WA, 98108

whitejh@wsdot.wa.gov.

Subject: Comments Dept of Transportation Project: SR509 Corridor Completion/I-5/South Access Road Project (due March 25)

Pulled together quickly but at least will provide some references to support public comment on Feb 27. Hope to add to these comments with more professional comments for March 25.

Thank you,

Arlene Brown

239 SW 189 PL

Seattle WA 98166

Home (206) 431-8693

arlene@mail.alum.rpi.edu

www.thirdrunway.homestead.com and also

www.nothirdrunway.homestead.com

Attached comments plus select pages from referenced web sites

Initial set of Comments for the Record

1) 509 extension Incompatible with Sea-Tac third runway - Kill the third runway since the region needs ground traffic improvement more than it needs a deadly short part time runway (FEIS admits increases aircraft ground incursions)

a) too close to unsafe MSE wall that is placing excessive load on area with soft soils. (see map with wall location at www.nothirdrunway.homestead.com/quake.html). MSE wall failure could result in slide as far as highway. Soft soil reaction to earthquake can cause movement of highway overpasses for up to an hour after quake causing structural failure such as occurred in California ( this is not just hypothetical!!).

b) destroys more wetlands - third runway already destroying too many- too many flooding problems already. Normandy Park homes on hills with no water in sight are getting flooded from underground stream movement.

c) reduces FOREVER the aquifer recharge and therefore available water, combined with the aquifer recharge loss from the third runway wetlands. We are losing too much water - terrorism threat less for underground water sources. 60 years from now when the contract with Seattle Water Dept runs out may be sole source drinking water aquifer. Could not find any concern from drinking water loss in your draft. Why?

d) too much construction traffic already from third runway. Already reduces traffic speeds by more than 15 miles per hour when trucks present.

e) too close to third runway safety area – toxic chemical hazard and falling airplane part hazards (Ask the children traumatized forever from airplane part falling in Mount Raineir school yard if you don’t believe this is a problem)

f) too noisy with increased highway noise plus increased runway noise - less trees to absorb noise. MSE wall will reflect noise into Burien and Normandy Park. Recent tree cutting and construction have already changed the noise in the area. You can already hear Highway 509 in the heart of Normandy Park due to changes in noise absorption over last few years.

g) Watershed can't handle the additional construction sediment and other pollutants

h) air can't handle the additional construction particulates and additional construction pollutants

2) South access road unacceptable.

a) too near wetlands and Des Moines . Aquifer may be within 2 feet of surface .

b) increases capacity of airport. Therefore triggers Clean Air Act diminimus limit (more than 100 tons of NOX) and a full up Clean Air Act conformity is REQUIRED. SEIS for third runway admitted Sea-Tac is " SURFACE TRANSPORTATION LIMITED ", (NOT runway space limited as Port propaganda machine portrays it). Additional 300 tons of NOx exceeds the 100 tons (80 tons?) NOX deminimus limit

c) NOx at airport contributes to Puget Sound ozone problems due to wind patterns and mountains. Need impact on ozone from additional airport related pollution the road will allow (ground traffic, air traffic, ground equipment).

d) too near runway protection zone (runway closest to terminal)so hazard from chemical pollutants, falling debri and ability to protect from terrorists

3) Comments applicable to all project

- 2 to 1 slopes unacceptable based on civil engineering best practices, FAA building advisory or regulation (and you are in the safety areas), 1998 King County Wetlands mitigation report, 1.2 million dollar repair of First Ave in Normandy Park (Miller Creek underneath didn’t have the 3 to 1 slope), etc

- Proposed mitigation such as covered trucks or trucks that only put as much fill in them that is legal to avoid dripping onto roads is NOT enforced and useless. See current third runway trucks for proof. Cheaper for them to pay the fines and haul maximum. Limited durations also ignored.

- Port of Seattle went on record that BMPs inadequate for North Employee parking lot project (significant amount of fill) at north end of airport (pollution fines for sediments in salmon bearing streams from what was first believed to be a water main break that turned out to be a spring popping out of nowhere– also got water on highway). The complexity of building on this water shed that has springs literally popping put of nowhere is well beyond BMP’s.

- Boring records are inconsistent.

- Port tests for soft soils used the wrong type of drill so not valid

- We have fractured till which needs to be considered when calculating contaminate transport speeds

- Where will the fill come from? How will it get there? How contaminated will it be? Reminder huge clean fill shortage due to proposed third runway and other Master Plan projects.

- Benzene levels around airport already significantly exceed the goal under Clean Air act with regard to 1 in million cancer risk (Contact Seattle-King County Dept of Health that has used the special 2001 EPA monitoring results at airport to calculate cancer risk). Benzene in combination with other chemicals makes the other chemicals more toxic. Proposal adds more benzene to an already toxic stew. Need risk analysis to determine illness and reduced life expectancy. Using this analysis need to determine a buy-out zone which is much greater than currently anticipated. Also to set maximum allowed pollution from airport since I assume you do not want to limit amount of highway traffic.

i) Air analysis focused on CO. It is airport activity NOx converting to ozone that is the real issue for Puget Sound (map of pollution concerns at http://www.ecy.wa.gov/pubs/0001003/fig-11.htm).

http://www.ecy.wa.gov/pubs/0001003/fig-09.htm shows that trend in people being exposed to unhealthy ozone levels is not necessarily going down. There was a huge spike in 1998 due to weather (almost 5 million people exposed to air not meeting federal health standards.) Full report at http://www.ecy.wa.gov/pubs/0001003/index.html.  EPA air trends web site gives specifics on exceedences.

j) Earthquake analysis needs to consider the recent SHIPS work

See faults at http://geohazards.cr.usgs.gov/pacnw/ships/brocher01/index.html. Note the dashed line running north and south in parallel to the Highway 509!!!!

Width of Seattle fault at http://geohazards.cr.usgs.gov/pacnw/actflts/sfzfig2a.html

Also note the velocity of the movement during the Feb 28,2001 earthquake at the airport was higher than anticipated and they are still trying to figure out why.

k) Both roads too close to airport runways and stored fuel. Too difficult to secure airport from terrorist activities

l) Giant sloth in Univ of WA museum found near airport not mentioned in your draft. But what you did cover was fascinating. Appreciate the effort.

# Attachment B: Airport Pollution and Health

## Airport Pollution Rankings and NY Asthma data

Sea-Tac was ranked tenth for people impacted by noise pollution. New York came in first and has a huge asthma death problem. The problem has increased significantly as the number of aircraft operations increased (coincidence?). The Sea-Tac health studies showed the area around the airport to have higher asthma for children than King County. King County was higher than Washington state so much higher that it actually inflates the statewide value for children (see Attachment C PowerPoint presentation or Childhood Asthma Hospitalizations King County, 1987-1996”, Public Health Data Watch, Volume 2, Number 1, Seattle-King County Department of Public Health, February 1998 available from public health, asthma links from  http://www.metrokc.gov).

Graphics that follow are from links from Safe Aviation for Everyone (SAFE) http://www.metronyaviation.org/

## Ozone Nonattainment for the top 50  airports

Topography as well as number of aircraft operations is one factor in ozone compliance. Obviously there are other sources of ozone as well. See Table 5 that follows

(from a link from Safe Aviation for Everyone (SAFE) http://www.metronyaviation.org/)

## NRDC Toxic Air Pollution Map

This map suggests that it would be better to tie SR 509 in with I-5 further south than the current plan.

Toxic Air Pollution 
Risk of Top Carcinogens in Major Metropolitan Areas

This May 1999 NRDC analysis presents, in map form, information on concentrations of carcinogenic air pollution in ten large U.S. urban areas and nine corresponding states, and calculates the total overall risk these combined toxics present. The analysis is based on data developed as part of the U.S. EPA's Cumulative Exposure Project.

Following information was copied from Natural Resources Defense Council site  http://www.nrdc.org/air/pollution/cep/csea.asp

Toxic Air Pollution Risk of Top Carcinogens in Major Metropolitan Areas Seattle, WA and Surrounding Area King County, which includes Seattle, has the highest risk in the state and the levels of air toxics are 203 times EPA’s safe* level of carcinogens in air. City names are in boxes. County names are unboxed. KEY *The U.S. Environmental Protection Agency has developed benchmarks for "safe" concentrations of toxics in air, levels at which one person in one million is at risk of developing cancer. Key represents the risk factor for a combination of 31 toxics as a multiple of EPA's safe level (e.g. darkest shade indicates levels more than 400 times EPA's safe concentrations). See the chart in the introduction for a list of the 31 toxics. RISK FACTOR AND SOURCE OF TOXIC AIR POLLUTANTS OF CONCERN IN KING COUNTY, WA Air Toxic Risk Source Percentage 1,3 Butadiene 73 Mobile 65% Chromium 40 Point 90% Formaldehyde 27 Mobile 73% Benzene 27 Mobile 77% Carbon Tetrachloride 13 Area 92% Mobile Sources: Cars, trucks, buses, tractors, etc. Point Sources: Large factories and other major industrial sources Area Sources: Small factories, dry cleaners, gas stations, etc.

=============================================================

# Attachment C: King County Health Data

See file arleneAtt C airhealth2001.ppt

# Attachment D: Partial copy of Nov 1999 Health, Air, Soil Comments to Corps

See Word file arleneAtt D Corps Nov99.doc

# Attachment E: Partial copy of Feb 2001 Health, Air, Soil Comments to Corps

See Word file arleneAtt D 3rdtry POSpermit.doc

# Attachment F: References and Bibliography (Partial List)

Sorry for the multiple formats but it allows me to find things. If I realized my first letter would develop into years of effort, I would have set up a database and used traditional formatting.

The letter identification switches to numbers after (xxx).

## References using letters

(a)	Supplement to the State Implementation Plan for Washington State, Plan for Attaining and Maintaining National Ambient Air Quality Standards for Ozone in Central Puget Sound, January 1993, Amendments June 1994

(b) 	Sea-Tac Airport Master Plan Update Draft Environmental Impact Statement (DEIS), 1995

(c)	Engineer’s Personal Assessment of the Sea-Tac Airport Master Plan Update Draft Environmental Impact Statement (DEIS) - Proposed Third Runway, The United States’ Most Expensive, Limited Capacity Runway, incorporated into FEIS response appendix.

(d) 	Sea-Tac Airport Master Plan Update Final Environmental Impact Statement (FEIS), 1996

(e) 	“State of WA Puget Sound Regional Council Final Noise Decision on Noise Issues”, dated 27 March 1996  (bolded by author to emphasize legal title)

(f) 	Comments on the Draft General Conformity for the Sea-Tac Airport Runway and Associated Development Projects, A. M. Brown dated April 30 1996

(g) 	Technical Report #8 prepared by P&D Aviation for Port of Seattle.

(h)	Testimony at the Congressional Aviation Subcommittee Hearing by nationally known economist Dr. Lynn O. Michaelis, held March 18, 1996

(i) 	Testimony at the Congressional Aviation Subcommittee Hearing by air transportation expert, Dr. Stephen Hockaday, held March 18, 1996

(j) 	Study submitted to FAA by Envirometrics, Dr. Ruby, Smith Engineering & Management, Cutler & Stanfield, dated 6 June 1996

(k) 	Implementation of an LDA/DME Approach to Runway 16R in lieu of a Third Runway at Sea-Tac, prepared by G. Bogan & Associates, Inc. dated 26 June 1995 (presumably submitted as comment to Draft EIS)

(l) 	Letter To PSRC President Doug Sutherland, From Pork Patrol, Al Furney, Chair, dated 12 June 1996  - in June 3-19,1996 PSRC correspondence package

(m) 	“City, State Forces Wrangle over Third Chicago Airport, Aviation Week & Space Technology, 8 April 1996

(n) 	GAO/RCED-95-35BR (Government Accounting Office)

(o) 	“Finally ! It’s Here (Denver International Airport Opens), Newsweek, 6 March 1995

(p) 	“Denver International Airport - Economic aspects”, Travel Weekly, 2 February 1995 v54, n9, p4

(q) 	“Montreal Airport never got quite off the ground” Times 15 April 1996 - in PSRC Correspondence package dated June 21-26,1996

(r) 	Comments regarding adding the part time dependent runway to the MTP. To D. Sutherland PSRC, From A. Brown, dated 15 June 1996 - in PSRC Correspondence package 3-19 June 1996. Special Note the cover letter enclosed a copy of 25 pages of comments dated 11 June 1996. These comments were hand delivered to the PSRC with the CASE comments on June 11,1996 so the July 19,1996v date is incorrect with respect to the pages labeled 1/25 and so on.

(s) 	“Comments on Public Comment Meeting June 27,1996 - Topic: Proposed Addendum to the 1995 Metropolitan Transportation Plan (MTP) to include the Third Runway”, To D. Sutherland & PSRC Executive Board, From A. Brown, dated 7 July 1996 - in PSRC Correspondence package July 10-11, 1996 (enclosure 3 in this Port Appeal letter of August 1996)

(t) 	Expert Noise Arbitration Panel Hearing December 1994

(u) 	FAA Hearing, Sea-Tac Airport,  June 1995

(v) 	PSRC Executive Boarding Meeting and Public Testimony, June 1996

(w) 	Letter (Supplement to FEIS Comments, “Draft conformity analysis does not support your conclusion that the project conforms to the State Implementation Plan”), To D. Ossenkop of FAA, cc Hinkel of Port, From U.S. Environmental Protection Agency, dated 6 June 1996

(x) 	Letter To PSRC, From D. DesMarais, dated 8 July 1996 - in PSRC Correspondence package June 26 - July 9, 1996

(y) 	“Executive Board Order, dated April 25,1995”, To PSRC, From Ravenna- Bryant Community Association, dated 8 May 1996 - in PSRC Correspondence package June 21-26, 1996

(z) 	Letter, To PSRC, From A. Brown, dated 10 April 1996 - in PSRC Correspondence package April 3-15, 1996

(aa) 	“Draft Amendment to MTP—Third Sea-Tac Runway, June 10, 1996 Order”, To PSRC, From North East District Council, dated 28 June 1996 - in PSRC correspondence package June 26 - July 9, 1996.

(bb) 	Letter, To D. Hinson of FAA, From R. Akers, dated 28 May 1996 - in PSRC correspondence package May 23-29, 1996.

(cc) 	ECO-088, To D. Ossenkop of FAA, From R. Parkin of U. S. EPA, dated 18 March 1996 - in PSRC correspondence package April 3-15, 1996.

(dd) 	Response to Requests for Supplemental Review, Addendum to the Flight Plan Project FEIS (1992) and Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport Final EIS (1996), PSRC, 10 July 1996.

(ee) 	Letter, To PSRC, From City of Normandy Park, dated 9 April 1996 - PSRC correspondence package April 3-15,1996.

(ff) 	“PSRC’s Resolution (A-93-03) and it’s Impact on Related Legislation”, To PSRC, From H. J. Frause, dated 1 April, 1996 - in PSRC correspondence package April 3-15,1996.

(gg) 	City of SeaTac Public Works Permit PWD0115-96, Parcel 282304-9016, Issued 6/20/96, Expiration 12/17/96, Contractor Segale, Signed by Bruce Rayburn

(hh) 	 “Number of Dirt Trucks Will Increase, Third Runway”, by V. Nordstrom, Highline News, 10 August 1996

(ii)	“Study: Bigger airport means more poor kids”, Highline News, 7 August 1996, page A7

(jj)	“Three Killed, 2 Hurt in SeaTac Wreck”, Highline News, 7 August 1996. page A1

(kk) 	“Airlines Draw Battle lines on User fee”, Seattle Times, 19 June 1996, page D1

(ll)  	“FAA Plans to Publish Draft Addendum to 1976 Agency Noise Policy by September”, Airport Noise Weekly, Volume 8, Number 11, dated 10 June 1996, page 81-82.

(mm) 	“Briefing Book”, Environmental Conservation Division, Northwest Fisheries Science Center, National Marine Fisheries Service, NOAA, January 1994 (entire book but especially page 24)

(nn) 	“Programs and Accomplishments”, Utilization Research Division, Northwest Fisheries Science Center, National Marine Fisheries Service, Seattle, WA, May 1995.

(oo) 	“Our Living Oceans, Report on the Status of U.S. Living Marine Resources”, Unites States Dept. of Commerce, National Oceanic and Atmospheric Administration, National Marine Fisheries Service, 1995

(pp) 	“Transfer of Land for Runway Underway”, Airport Noise Report, Volume 8, Number 12, 8 July 1996, page 94.

(qq) 	“Dramatic Drop in our infant mortality rate”, Post-Intelligencer, 2 August 1996, pages C1, C4 (drop NOT applicable byairport)

(rr) 	“ATA Questions Validity of Airport Construction Needs Study; Says Adequate Funds Exist for Necessary Airport Projects”, ATA News, Air Transport Authority of America, 20 March 1996

(ss)	“Rockwell has won back the Global Positioning System (GPS) satellite contract”, The Composites & Adhesives Newsletter, July-September 1996, page 3.

(tt)	“Notice of Decision by the Port of Seattle”, Public Notices, Seattle Times, 8 August 1996

(uu)	“Air Pollution, Council’s report based on Epidemiological study”, by R. Kassel, National Resources Department Council Urban Environmental Program Sr. Attorney, Post-Intelligencer, 16 June 1996, page E3.

(vv)	“Flying Off-Course: Environmental Impact of America’s Airports”, National Resource Defense Council, October 1996

(ww)	“Waste Clean Up, Safe and Sound?”, Highline News, 23 November 1996, pages A1, A7 (additional information supplied by a participant)

(xx)	“Third Runway Battle, The Big Dirt Haul”, Highline News, 16 November 1996, pages A1, A2 (Shows map of potential haul routes referenced in FEIS (ref. d))

(yy)	Engineering Principles of Ground Modifications, by Manfred R. Hausman, McGraw-Hill Publishing Company, New York

(zz)	Soils in Construction, Third Edition, by W/. L. Schroeder Prentice Hall, New Jersey

(aaa)	“Sea-Tac Third Runway to get its fill of dirt”, Seattle Times 15 August 1996 pages A1, A19 (runway 14 feet below FEIS assumptions)

(bbb) Letter to FAA. D. Ossenkop, From Mary Riveland, Director WA DOE, dated 20 December 1996

(ccc) 	49 U.S.C, 47101 et. seq. (formerly Airport and Airway Improvement Act, Section 509, paragraph (7) (A))

(ddd)	Washington State Legislature Release, “ South King County Lawmakers Question Approval of the Third Runway Plan”, dated 20 December 1996.

(eee)	“DOE Gives OK to Runway”, Highline News, Page A7, December 21,1996

(fff) 	“ Dust Emissions at North SeaTac Park”, Puget Sound Air Pollution Control Agency Notice of Violation No. 35809, Registration No. P371603874-75, Regulation I, Section 9.15 (a) : Emission of Fugitive Dust without use of best available control technology, 8 August 1996

(ggg)	Letter regarding Snow Equipment Storage Shed Environmental Checklist and Determination of Nonsignificance, From Port of Seattle, Barbara Hinkle to Debi DesMarais, 25 July 1996

(hhh)	“Asbestos Delays North SeaTac Work”, Highline News, 13 July 1996, page A8

(iii)	“Plane Crashes at SeaTac”, Highline News, 24 August 1996, page A1

(jjj)	“Girl Struck, dies in I-5 Jam Detour”, Highline News, 4 September 1996, page A1

(kkk)	“Infant Death Rates Still Higher Here”, Highline News, 6 October 1996, page A3

(lll)	FAA report “Impact of Boeing Field Interactions on the Benefits of the new proposed runway.” Feb. 1993

(mmm)  “Draft Sea-Tac Mitigation Study”, Burien - Airport Assistance and Mitigation Studies, Hellmuth, Obata and Kassabaum (HOK), 21 October 1996, Final to be released March 1997

(nnn)	Appeal of the Adequacy of the FEIS for the Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport, Filed by City of Sea-Tac

(ooo)	Appeal of the Adequacy of the FEIS for the Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport, Filed by Akers

(ppp)	Appeal of the Adequacy of the FEIS for the Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport, Filed by Cities of Des Moines, Burien, Federal Way, Normandy Park and Tukwila, Highline School District 401, Airport Communities Coalition

(qqq)	Lawsuit filed by Cutler & Stanfield, Filed by Cities of Des Moines, Burien, Federal Way, Normandy Park and Tukwila, Highline School District 401, Airport Communities Coalition

(rrr)	Earth Pressures and Retaining Walls, Whitney Huntington, John Wiley & Sons, NY, 1957

(sss)	“ Different Dirt, FAA Rejects fill plan to extend airport runway in Albuquerque”< Highline News, January 29,1997, page A1

(ttt)	“Environmental Assessment for Proposed Improvements to Runway 3-21, Albuquerque International Airport”, prepared by Coffman Associates, Inc. June 1994

(uuu) 	Sea-Tac Noise Exposure Update, June 1982

(vvv)	Draft Supplemental Environmental Impact Statement for the Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport (DSEIS), 1997.

(www) 	World Wildlife Fund Newsletter, “Focus”, March/April 1997, Volume 19, Number 2

(xxx) 	“A Comparison of FAA Integrated Noise Model Flight Profiles with Profiles Observed at Seattle-Tacoma Airport” by George W Flathers, December 1981, Office of Environment and Energy Project 1494A, Contract DTFA01-82-C10003, Mitre: Metrek Division

## Additional References (note changes to numbers)

- Electronic mail, A. Brown, Myrtle Jones, Hydrologist, US Geological Services,April 16, 1998

2)	Electronic Mail Gary Turney, Supervisory Hydrologist, US Geological Services, April 16, 1998

3)	Leisch, Brice A. , Price, Charles E. and Walters, Kenneth, L, Geology and Ground-Water Resources of Northwestern King County, Washington, Washington State Division of Water Resources Water Study Bulletin No. 20, 1963

4)	Luzier J.E., Geology and Ground-Water Resources of Southwestern King County, Washington, State Dept. of Water Resources Water Supply Bulletin No. 28, 1969

5)	Richardson, Donald, Bingham J.W. and Maddison R. J., Water Resources of King County, Washington, U.S. Geological Survey Water-Supply Paper, 1852

6)	Woodard, D. G. Packard, F. A., Dion, N.P. and Sumioka, S.S., Occurance and Quality of Ground Water in Southwestern King County, Washington, U. S. Geological Survey, Water- Resources Investigation Report 92-4098, 1995

7)	AGI Project 16,116.001, Draft Groundwater Quality Impact Evaluation Proposed North Employee Parking Lot Seattle Tacoma International Airport, SeaTac Washington, AGI Technologies, 11 April 1997

8)	AGI Project 16,116.001, Groundwater Quality Impact Evaluation Proposed North Employee Parking Lot Seattle Tacoma International Airport, SeaTac Washington, AGI Technologies, 13 June 1997

9)	Request for Public Hearing and Comments on Port of Seattle File Number 96-4-02325”, Notice of Application for Water Quality, From A. Brown, dated 8 January 1998

10)	Wetlands/Water Hearing Comments submitted by A. Brown, April 9, 1998

(includes Sea-Tac 24  hour maximum rainfall data)

11)	Wetlands/Water Hearing Cassette Tape, April/May 1997 Weekend Headliner: Safe Skies, Safe Water by Ross Simpson, NBC News Extra. Submitted by Debi Wagner at Hearing April 9, 1998 (Zinner of WA DOE interview regarding de-icer pads)

12)	Hillis, Clark, Martin & Peterson,” Re: Lone Star Northwest’s Sand and Gravel Quarry, Maury Island”, To Mark Mitchell, dated 24 February 1998

13)	Hillis, Clark, Martin & Peterson,” Lone Star Northwest’s Sand and Gravel Quarry, Maury Island”, To Fred White, dated 19 February 1998.

14)	Cutler & Stanfield comments on Air Conformity Determination (contains the Univ of Florida fill calculations).

15)	Cutler & Stanfield comments on Passenger Facility Charges

16)	Sierra Club Cascade Sound April/May 1998 newsletter

18) 	Hotel correspondence B. Shurling and Port of Seattle

19)	Caufman Report (1.5 dB)

20)	Risk of a Fatal Large Jet Transport Bird Strike, web http:/airsafe.com/birds/birdrisk.htm

21)	Twenty Worst Aviation Accidents, web http://www.primenet.com/~kebab/worst.htm

22)	City reshaped: up and down, (Denny Regrade), web http://www.seattletimes.com:80/education/centennial/march/reshaped.html

20) Draft NPDES, for SeaTac Airport (incomplete title), 1997 – note ref number error

23)	NPDES for SeaTac Airport (incomplete title), 1998

24)	Comments on Sea-Tac Airport Draft NPDES, A. Brown, 10 December 1997.

25)	NPDES Proposed Waste Discharge Permit No. WA-002465-1, Port of Seattle, Seattle-Tacoma International Airport, Response to Comments, Public Meeting Held November 3, 1997 and November 10, 1997, prepared by Lisa Zinner, P.E. 20 February 1998.

26)	Conveyer Presentation to Des Moines City Council

27)	Comments on Sea-Tac Airport SEIS due 31 March 1997, From A. M. Brown, To FAA, Dennis Ossenkop, 28 March 1997

28)	Request for Public Hearing on “Port of Seattle File Number 96-4-02325”, Notice of Application for Water Quality Certification and For Certification of Consistency with the Coastal Zone Management Program, From A. Brown, To Corps of Engineers & DOE, 30 December 1998

29)	Public comments & written submittal, Public Hearing Port of Seattle File Number 96-4-02325”, Wetlands Permit, Notice of Application for Water Quality Certification and For Certification of Consistency with the Coastal Zone Management Program,  From A. Brown, To Army Corps of Engineers & Dept of Ecology (DOE), 9 April 1998

Third Set of Comments on “Port of Seattle File Number 96-4-02325”, Wetlands Permit, Notice of Application for Water Quality Certification and For Certification of Consistency with the Coastal Zone Management Program, From A. Brown, To Army Corps of Engineers & Dept of Ecology (DOE), 15 April 1998

Addendum to Third Set of Comments on “Port of Seattle File Number 96-4-02325”, Wetlands Permit, Notice of Application for Water Quality Certification and For Certification of Consistency with the Coastal Zone Management Program, From A. Brown, To Army Corps of Engineers Dept of Ecology (DOE), 19 April, 1998

CASE comments supplied in meeting held 15 May 1998, Col. Rigsby and J. Freedman (Arlene Brown, Larry Corvari, Al Furney, Jim Bartlemay also in attendance)

Des Moines Creek Basin Plan, Des Moines Creek Basin Committee, City of Sea-Tac, City of Des Moines, Port of Seattle, and King County, November 1997

“Toxics: Out of Site but on our minds”, Sound & Straits Newsletter, Volume 8, Number 1, People for Puget Sound, February 1998, pg 7 [“Puget Sound...some of the most severely contaminated sediments in the country”]

Public Hearing on DOE and Port of Seattle Agreement on Ground Water Study at Airport, Burien Library, May 21,1997

Comments on DOE and Port of Seattle Agreement on Ground Water Study at Airport, To DOE, Roger Nye, From A. Brown, dated 8 June 1997

”Runway Project to Start Again”, Highline News, Pg. A6, by Marc Stiles, 11 December 1996 (Runway Safety Area 1996 20,000 trucks only able to haul 350,000 of the 450,000)

Memorandum of Agreement or memo?, From Anita Frankel of EPA Region 10, To Lowell Johnson, FAA NW Mountain Region, Regarding requiring delay in construction of North Terminal to comply with Air Conformity, 23 August 1996

Supplemental Environmental Impact Statement for the Proposed Master Plan Update Development Actions at Seattle-Tacoma International Airport, 1997. (SEIS)

US Department of Transportation FAA, Northwest mountain Region, Record of Decision for the Master Plan Update development Actions, Sea-Tac International Airport, 3 July 1997

“1997 Air Quality Annual report for Washington State”, WA DOE Publication Number 97-208.

“1997 Air Quality Data Summary”, WA DOE Publication Number 98-212.

“Sea-Tac International Airport Proposed Third Runway Project”, To Corps of Engineers Jonathan Freedman, From Joseph A. Pobiner, AICP, Associate Principal, Director – The PGAL Planning Group. 14, April 1998  (earthen berm seismic potential, slide, storm water-run-off issues)

Part 150 Passenger Facility Charge Application, Port of Seattle for Seattle-Tacoma International Airport, 1995

Part 150 Passenger Facility Charge Application, Port of Seattle for Seattle-Tacoma International Airport, 1998

Meeting, Army Corps of Engineers (Col. Rigsby, J. Freedman), RCAA (A. Furney), CASE (A. Brown, J. Bartlemay, L. Corvari), Seattle Headquarters, 15 May 1998. (Included seismic maps, bird hazard and runway incursion data)

Meeting, Army Corps of Engineers (J. Freedman, T. Mueller (part time), G. Terzi), RCAA (A. Furney), CASE (A. Brown, L. Corvari), C. Gower, Seattle Headquarters, 7 August 1998

Meeting, Army Corps of Engineers (J. Freedman, G. Terzi), RCAA (A. Furney), CASE (L. Corvari), C. Gower, Seattle Headquarters, xx 1998

Seattle Citizen TV Show, Topic (not the official title) Cedar Water shed - How to save salmon, Guests Charles Raines Cascade and Director Gale of Seattle Public Utilities, 9 August 1998.

Letter From Dan Caldwell, Regarding use of Highline Water by Seattle during early 1990’s El nine weather, Provided to Army Corps of Engineers by CASE in 1998.

Letter, From Jennifer Belcher, Director of Public Lands, Dept. of Natural Resources, To Arlene Brown, dated 18 June 1997 (Confirms Surface Mine Land Reclamation Permit needed for borrow pit sites 1, 2 and 3)

Supplemental SEPA Determination and SEPA Determination of Non-Significance (DNS) of Proposed Action, Seattle-Tacoma International Airport Master Plan Improvements – Wetland Mitigation, 6 August 1998.(Auburn Wetlands, comments due Aug 21, 1998)

Comments on Port’s Wetlands Mitigation (in Auburn) due Aug. 21. From A. Brown, To Port of Seattle, 13 August 199

Letter, From Port of Seattle, Barbara Hinkle, To Arlene Brown, no title (Port’s Response to A. Brown’s comments on Auburn Wetlands mitigation), dated 9 September 1998 (“BMPs inadequate”)

Note: some of the data from the following 7 health references may be available at the http://www.metrokc.gov/health/ web site (Public Health, asthma)

Letter, From Heimann, Nita and Sullivan, Marianne of Seattle-King County of Department of Public Health, To Lorna Dove, Georgetown Crime Prevention and Community Council, (health statistics for census tracts 109 and 112 prepared June 1997), 20 June 1997

Letter, From Smyser, Michael of Seattle-King County of Department of Public Health, To Scully, Robert of the Seattle Neighborhood Planning Office, “ Georgetown Health Indicators”), 20 August 1997

“Childhood Asthma Hospitalizations King County, 1987-1996”, Public Health Data Watch, Volume 2, Number 1,Seattle-King County Department of Public Health, February 1998

“The Health of King County—Highlights”, Public Health Data Watch, Volume 2, Number 1, Seattle-King County Department of Public Health, August 1998

“The Health of King County” (full report), Seattle-King County Department of Public Health, 1998

“Healthy Youth in King County—Highlights”, Public Health Data Watch, Volume 2, Number 1, Seattle-King County Department of Public Health, October 1999.

“Addressing Community Health Concerns around SeaTac Airport Progress Report on the Work Plan Proposed in August 1998”, prepared by WA State Dept. of Public Health, 25 February 1999.

“Toxicity of Aircraft De-icer and Anti-icer Solutions to aquatic Organisms”, Hartwell, s. Ian, Jordahl, David M., May, Eric B., Maryland Department of Natural Resources, Tidewater Administaration, Chesapeake Bay Research and Monitoring Division, Fisheries Division, Annapolis, Maryland, May 1993.

“Airplane emissions: A source of mutagenic nitrated polycyclic aromatic hydrocarbons”, CASE Western University, Cleveland, Ohio, 1986. (nitroarenes)

De-icing Blamed for Pollution, Researcher says liquids entering ground water near airport”, Sorenson, Eric, Seattle Times, 10 January 1999 (quotes WWU Devon Cancilla “very toxic stew”)

“Aircraft spread deadly viruses”, London Reuter, 26 June 1997,

“Kids Near airports don’t read as well because they tune out speech, Cornell study finds”, Lang, Susan, Science News, 28 April 1997.

“Aircraft Noise, A potential Health Hazard”, Bronzaft, Arline L., Dee Ahern PhD,RN, Kathleen, Mcginn, regina, MD,FACP, January 1998.

Occupational Factors Associated with Astrocytomas: A Case Control Study; American Journal of Industrial Medicine

Air Pollution and Your Health: The Report

Health Effects of Outdoor Pollution; American Family Physician

Breathless; Natural Resources Defense Council

Particulate Air Pollution as a Predictor of Mortality in a Prospective Study of US Adults; Respiratory Critical Care Medicine

Atmospheric Reactions of Polycyclic Aromatic Hydrocarbons; University of California, Riverside

An Association Between Air Pollution and Mortality in Six US Cities; New England Journal of Medicine

A critical Review of the Health Effects of Atmospheric Particulates; Toxicology and Industrial Health

Health Effects of Particulate Air Pollution: Time for Reassessment?; Environmental Health Perspectives

Environmental Risk Factors for Primary Malignant Brain Tumors;  Review; Journal of Neuro-Oncology

“Breast Cancer & the Environment, The Estrogen Connection”, by Batt, Sharon and Gross, Liza, Sierra, September/October 1999. pages 40-41.(“synthetic organic estrogens, such as those in some plastics, fuels, and pesticides, appear to increase risk’)

“Cancer County”, Sierra (magazine), September/October 1999. Page 17.

“Air Pollution by Jet Aircraft at Seattle-Tacoma Airport”; Donaldson, Wallace r. Of National Weather Service Office Seattle-Tacoma, WA, ESSA Technical Memorandum WBTM WR 58, US Department of Commerce, Environmental Science Services Administration, Weather Bureau, salt Lake City, Utah October 1970.

President Clinton issued Executive Order 12898, “Federal Actions to Address Environmental Justice in Minority and Low-Income Populations”, President Clinton, 11 February 1994.

“No sugar coating this report on carcinogens”, US News & World Report, 27 September 1999(National Toxicology Program year 2000 Report on carcinogens to increase risk for 1-3, butadiene, ethylene oxide (antifreeze) , dioxin & 10 others)

EPA Web site for some chemicals and their hazards: www.epa.gov/ttn/uatw/hlthef/.Need to access via www.epa.gov.

Acrolein data on EPA site www.epa.gov/ttn/uatw/hlthef/acrolein.html

Arsenic data on EPA site www.epa.gov/ttn/uatw/hlthef/arsenic.html

Benzene data on EPA site www.epa.gov/ttn/uatw/hlthef/benzene.html

1,3-Butadiene data on EPA site www.epa.gov/ttn/uatw/hlthef/butadien.html

Formaldehyde data on EPA site www.epa.gov/ttn/uatw/hlthef/formalde.html

EPA, Integrated Risk Assessment Information System www.epa.gov/npispgm3/iris/

Los Angeles Air Toxicity at www.house.gov/waxman (benzene, butadiene, formaldehyde)

Environmental Defense Fund web site www.edf.org, link to scorecard (pollution by zip code)

From Frost of DOE, To A. Brown per her request, 1998-1999 air pollution data from special SeaTac study. November 1999. subsequent draft report dated December 1999.

“Rock, Andrea, “Toxicville”, Ladies Home Journal, September 1999. Pg 106-109, 114-116.

“Atmospheric Transformation of Air toxics: Benzene, 1,3-Butadiene and Formaldehyde” available at www.epa.gov:80/ordizux/regs/toxics/airtoxla.pdf

SeaTac Air Quality – Final Report, ESL-ET59, (POS 20383 stamped on it), by Adams, R, Hulet, B., Ramras, D., Seidman, H. et al, ESL Incorporated, 28 June 1973 (750% formaldehyde limit) Available Health section of CAW website www.nonoise.org/quietnet/us-caw/

Mobile Source Hazardous Air Pollutant Emissions in the Sea-Tac Urban Area.  Radian Corp, 1994.

Crutcher, E. R., To Moore, Shawn of AMTEST, Microlab test report 036-95, AMTEST #95-03664-03667, 2 March 1995. (clothesline, gutter, rafter) (copy in one of the EIS’s)

Air Quality Survey Sea-Tac International Airport.  McCulley, Frick & Gillman, Inc., 1995.

Comments on Frick SeaTac Air report by Debi DesMarias/(now Wagner) Available Health section of CAW website www.nonoise.org/quietnet/us-caw/

1996-1997 Carbon Monoxide Saturation Study Sea-Tac International Airport Area.  Washington State Department of Ecology (WSDOE), 1997.

Illinois EPA Strategy for Continued Assessment of O’Hare Airport Air Toxics Emissions Impact on Surrounding Communities, Skinner, Thomas Director Illinois EPA, Proposal 28 June 1999.

“Estimation and Evaluation of Cancer Risks Attributed to Air Pollution in Southwest Chicago”, by Summerhays, John, US EPA, Region 5 Chicago Illinois, September 1989.

“Estimation and Evaluation of Cancer Risks Attributed to Air Pollution in Southwest Chicago.” ViGYAN Inc. to US-EPA Region V. 1993. p. B-33.

Memorandum of Agreement, Air Quality Monitoring Program Activities Relating to the Seattle-Tacoma International Airport Vicinity, EPA, DOE, PSABCA, Port of Seattle, dated 10 October 1996

Letter,  “Lack of Enforcement of Requirements to Use State Facilities”, from Senator Julia Patterson, To Sid Morrison, Secretary Washington State Department of Transportation, dated November 19,1998 (truck hauling)

“Air Traffic and Operational data on Selected US Airports with Parallel Runways, by Doyle, Thomas M., McGee, Frank G, NASA /CR-1998-207675, May1998 (file AB S1)

“Runway incursions Affect An Airline Pilot Every Other Day”, by Capt. Tom , Air Line Pilot, February 1999 (ALPA web site under Publications) (file AB S1)

“Financial Commitments needed to enhance the safety of the airport and air traffic control system”, John O’Brien Director Engineering & air Safety Department ALPA, testimony before Subcommittee on Aviation US House of Representatives, 4 February 1999 (ALPA web site) (file AB S1)

“Parallel runway requirement analysis study” Volume 1, NASA-CCCR-191549-VOL-1, by Ebrahimi, Yaghoob S. 1 December 1993

“Parallel runway requirement analysis study, Simulation manual” Volume 2, NASA-CCCR-191549-VOL-2, by Ebrahimi, Yaghoob S. 1 December 1993

“Reliability Modeling and Methodology for Independent Approaches on parallel Runway Safety Analysis, by Babcock, P., Shor, A. and Rosch, G. NASA CR-198-207660, April 1998. (file AB S1)

“Why a Little More Traffic Makes a Lot More Runway Incursions”, by Lounsbury, Lincoln, Air Line Pilot, May 1999 (ALPA web site) (grow exponentially) (file AB S1)

“Results of Monitoring King County Wetland Mitigations”, by Anna Mockler et al, King County Dept. Of Development and Environmental Services, 4 August 1998.

“Evaluation of Retaining Wall/Slope Alternatives to Reduce Impacts to Miller Creek, Embankment Station 174+00 to 186+00”, prepared by HNTB and/or Hart Crowser, Inc.(no reponsible person or organization listed on report), 1999.

Letter, To Tom Luster of DOE, From Jerald LaVassar, DOE, “Evaluation of Retaining Wall/Slope Alternatives to Reduce Impacts to Miller Creek, Embankment Station 174+00 to 186+00” dated 9 August 1999

Letter. To Robert T. Maruska of HNTB, From Thomas M. Gurtowski of Shannon & Wilson, dated 27 March 1999.

Koshusho, Takegi (Prof Chui Univ), “Water Film in Liquified Sand and Its Effect on Lateral Spread”, Journal of Geotechnical and Geoenvironmental Engineering, ISSN 1090-0241, Volume 125, Number 10, October 1999, pgs 817-831. (ongoing deformation, embankment loading)

Lee, K. M., Shen, C. K., Leung, D.H.K. and Mitchell, J. K., “Efffects of Placement Method on Geotechnical Behavior of Hydraulic Fill Sands”, Journal of Geotechnical and Geoenvironmental Engineering, ISSN 1090-0241, Volume 125, Number 10, October 1999. Pg 832-845 (compositional factors)

Fox, Patrick, “Solution Charts for Finite Strain Consolidation of Normally Consolidated clays”, Journal of Geotechnical and Geoenvironmental Engineering, ISSN 1090-0241, Volume 125, Number 10, October 1999. Pgs 847-867. (FEM, pore pressure predictions for soft soils)

Leshchinsky, Dov (Discussion )“Limit Analysis versus Slope Stability”, Journal of Geotechnical and Geoenvironmental Engineering, ISSN 1090-0241, Volume 125, Number 10, October 1999.pgs 914-915.

Yu, H. S., Salgalso, R., Sloan, S. W., and Kim, J.M. (closure )“Limit Analysis versus Slope Stability”, Journal of Geotechnical and Geoenvironmental Engineering, ISSN 1090-0241, Volume 125, Number 10, October 1999.pgs 915-918. (slope stability graphs of different angled slopes)

Engineering Manual EM 1110-1-1804 Geotechincal Investigations, Department of the Army, 29 February 1984 (excludes roads and airfields)

Whitely, Peyton, “State’s tallest noise walls going up along Highway 520”, Seattle Times Eastside bureau, 4 August 1998 (38 feet high sunk 20 feet in ground)

“Recent developments in Landslide Mitigation Techniques (Part 2)”, http://www.geolith.com/publications/recent_devel/recent_devel.htm

Regional Commission on Airport Affairs, Presentation to Des Moines City Council Feb.11, 1999 (costs and airlines’ concerns)

“Candidates for Port focus on growth, jobs”, Seattle-Post Intelligencer, 11 October 1999 (Commissioner Claire Nordquist “doubling the airport’s capacity”)  (file AB FP2 126)

Clean Water Act/Wetlands Public Hearing, File 1996-4-02325, Public Notice Date 30 September 1999, Foster performing Art Center, 3 November 1999 (exceeded capacity)

FAA Advisory Circular 150/5200-33, “Hazardous Wildlife Attractants on or Near Airports”, dated 1 May 1997.

Letter, Port of Seattle, To Dear Caller (multiple callers so sent form letter), regarding lost Antonov 124 Freighter, Incident 10 November 1998, wrong airport, “averaged 2000 feet”, dated 16 November 1998.

Addendum to IWS Engineering Report, Seattle-Tacoma International Airport, Volume 1, Kennedy/Jenks Consultants. April 1998. (AKART, de-icer pad insufficient room, too expensive)

Port of Seattle Memorandum Item 8a, Meeting date 10 March 1998, “Request Port of Seattle Commission Authorization for the General manager, Airfield Line of Business and the Director of Engineering Services to reject all bids, readvertise for bids and award a major construction contract for the Third runway: Embankment Construction- Phase I” 26 February 1998 (bids non-responsive or 23 to 48% over estimate)

Regional Airport System Plam1988-2020, Air Transportation element of the regional Transportation Plan, Puget Sound Council of Governments, September 1988. (“expansion within existing property” pg vi)

“Final report, Master Plan Update for Sea-Tac International Airport, PEAT MARWICK/TRA, for Port of Seattle, September 1985. (no 3rd runway  - environmental impact pg 1, underestimated operations pg 4-2)

Airtrac Washington, State Transportation Commission, Final report and Policy Recommendations, November 1993 (“design capacity 2005-2010”)

The Polluted Waters Report, Puget Soundkeeper Alliance, 1997.

Coho Salmon, Puget Sound/Strait of Georgia ESU, Candidate Listing, National Marine Fisheries Service, Northwest Region, Protected Resources Division, July 1995 (AB FS1 136)

Stelle, William Jr., “The Pacific Salmon Challenge: Merging Concepts of Water Quality and Aquatic Health”, National Marine Fisheries Service, December 1998.(AB FS1 137)

Hillman, T. W., Stevenson, J. R., Snyder, D. J., “Assessment of Spawning Habitat in three Puget Sound Streams, Washington”, report to Airport Communities Coalition, April 1999. (AB FS1 138)

Miller Creek Watershed, Dept. Of Landscape Architecture, University of Washington, Class of Winter 1972 quarter under direction of Professor David Streatfield (AB FS1 139)

Ames, James, “Miller Creek: Present Staus and Potential for Salmon Production”, Wasington department of Fisheries, 1970.

Haughland and Sherrow, Plaintiffs First Interrogatories to Defendant King County, Willis W. Kludt vs King County; Port of Seattle, and Washington State Highway Commission, 1972.

Environmental Materials Transport Community Newsletter June 1998

Environmental Materials Transport video 1998

OPA Press Release: Labor secretary calls for an end to Silicosis [10/31/96] (Munzer silicosis) http://www.osha-slc.gov/OshDoc/Other_Agency_data/MEM19960502.html

Canning, Kathie, Harrigan, Kate, “Research Critical to Understanding Endocrine Disrupters”, Pollution Engineering, September 1999, page 3

Web site http://nationalacademies.org/cls/best/reports.html

“Arsenic in Drinking Water”, Subcommittee on Arsenic in Drinking Water, National Research Council, 1999.

“Hormonally Active Agents in the Environment”, Committee on Hormonally Active Agents in the Environment, National Research Council, 1999

Flight Plan Project, Final Programmatic EIS (pg 4-99 Moses Lake)

Port of Seattle letter, from Gina Marie Lindsey, Director Aviation Division, To Barbara Stuhring, dated 31 October 1997 (two express purposes)

Seattle-Tacoma International Airport, Capacity Enhancement Plan Update, July 1995 (also available on web)

SEA-Seattle-Tacoma Intl Airport, Seattle WA, Airport Information Published on 9 September 1999. AirNav Web site http://www.airnav.com/airport/SEA (airport data including elevation, obstacles)

Memorandum CENPS-OP-RG, Seatac EIS, From Jack Kennedy, Army Corps of Engineers Regulatory Branch, 14 August 1995 (so it is referring to DEIS, wetlands mitigation, purpose)

“Third Runway”, Thomas, Will, The News, 2 October 1996 (church wetlands prevent house building. Subterranean fed wetlands)

Corbett, James J and Fischbeck, “Emissions from ships. (pollution and policy implications), Science, Electronic collection A19998018231, 31 October 1997. (highest amounts of pollution of all combustion sources per ton of fuel consumed 1-3 days residence times”)

Schwarz, S. E., Science 243, 753, 1989. (Nitrous oxide residence times)

Scott, William B, “Report Claims Aircraft Can Influence Climate”, Aviation Week, 30 August 1999, page 57.

Wood, Warren, Kraemer, Thomas F., and Hearn Jr., Paul P., “Intragranular diffusion:an important mechanism influencing solute transport in clastic aquifers?”, Science, v247, n4950 p1569, 30 March 1990.

Anderson, Eric E., Talley, Wayne K., “The oil spill size of tanker and barge accidents:determinants and policy implications”, Land Economics, v71, n2, May 1995, p216

McKenna, James T., “FAA Aims to revive Runway Safety Fight”, Aviation Week, 1 November 1999, page 40-41

“Impacts Of Deicing Fluids On Elijahs And Gunpowder Creeks”, Boone County, Kentucky, Kentucky Department for Environmental Protection, Division of Water, Frankfort, Kentucky. Available online http://water.nr.state.ky.us/dow/elijah.pdf

Johnson, Glen, “More Close Calls at Airports Incidents Up Despite Efforts to Reduce Near-misses on airport runways are getting more frequent”, The Associated Press, 8 August 1999. (see Appendix K)

“Sensitivity of Fish Embryos to Weathered Crude Oil: Part I. Low-Level Exposure During Incubation Causes Malformation, Genetic Damage, and Mortality in Larval Pacific Herring (Clupea Pallasi)” by Mark. G. Carls, Stanley D. Rice, and Jo Ellen Hose, Environmental Toxicology and Chemistry, Vol. 18., No. 3., pp.481-493, 1999

“Making Endangered Species Act Determinations of Effect for Individual or Grouped Action at the Watershed Scale” prepared by the National Marine Fisheries Service Environmental and Technical Services Division Habitat Conservation Branch, August 1996

“Sea-Tac International Airport Impact Mitigation Study, Initial Assessment and Recommendations”, prepared under a grant from the State of Washington by Helmuth, Obata & Kassabaum Inc., et al., February 1997

Perdue, Nancy Jo, “Salmon Spotted in Creek”, The Highline Times, 17 November 1999. (Dusenbury – 200 coho salmon in Des Moines Creek)

Addressing Community Health Concerns Around SeaTac Airport: Second Report on the Work Plan Proposed in August 1998, WA Public Health Department, December 1999

“Dropout rates brutally honest”, Seattle Times, 21 November 1999. Pages B1, B2 (source Office of Superintendent of Instruction, 34% Highline, State 16.4, Seattle 10.9) (file AB H1 169)

Harrington, Patrick, “Auditor finds Port’s books in poor shape”, Seattle Times, 6 November 1999, (file AB FP2 170)

Tacoma-Seattle area susceptible to deep, killer quake, magazine says”, The News Tribune, 29 October 199, page B2. (6.5 magnitude intraslab quake below Sea-Tac Airport in 1965 killed seven.) (file AB FEQ1 171)

Gower, Chris, Comments to Corps of Engineers and WA DOE, “Public Notice of Application for Permit dated September 30, 1999, Proposed Third runway at Seattle-Tacoma International Airport, dated 8 November 1999.

“Appeals court rules for third runway at Seattle-Tacoma International Airport”, Seattle Times, 16 November 1999.

“Cancer Care Report Annual Report 1991”, Highline Community Hospital.

“Cancer Care Report 1992”, Highline Community Hospital.

“Cancer Care Report, 1994 Annual Report, 1993 Statistical Review”, Highline Community Hospital, 1994.

“Cancer Care Report Annual Report 1995, 1994 Statistical Review”, Highline Community Hospital

“Cancer Care Report 1996 Annual Report, 1995 Statistical Review”, Highline Community Hospital

Cancer Care Report 1997 Annual Report, 1996 Statistical Review”, Highline Community Hospital

Cancer Care Report 1998 Annual Report, 1997 Statistical Review”, Highline Community Hospital

Cancer Care Report 1999 Annual Report, 1998 Statistical Review”, Highline Community Hospital, Burien Washington.

“Cancer Facts and Figures”. American Cancer Society. Data for years 1991-1997.

NIH Guide: Health Disparities: Linking Biological and Behavioral Mechanisms with Social and Physical Environments, RFA: ES-00-004, National Institute of Health (NIH), Released 4 November 1999. (file AB H1 183)

“Special Report: Hushkits: What they are, what they do, and What’s certified for Aircraft Types”, Airport Noise Report, Volume 11, Number 6, 16 April 1999. (noise model doesn’t have hushkits)

Lamberton, Jack, What Causes Brain Tumors? From Well-Connected, Lycos Health Topics A-Z, September 1998. http:\\Webmd.lycos.com/topic_summary_artcle/DMK_ARTICLE_5461950 (file AB H1 185)

Technical Information and Publications, Soft Soil Stabilization, Polyfelt Geosynthetics, web site www.polyfelt.com/technica.htm. October 1999. (extensive references) (file AB FEQ1)

02803 – Retaining Walls. Web site 4specs.com/s/02/02830.html. October 1999. (file AB FEQ1)

Project Report, Grand County sets a World Record”, Yenter Company, www.yenter.com/Projects/grandcounty.html (reinforced soil walls in 1997...world record 55 feet high), (file AB FEQ1)

Quinn, Barbara, “Finding a Better way to Manage Runoff”, Pollution Engineering (Cahners), August 1999, page 25.

“DOJ to Appeal Decision on Air Quality Standards”, Pollution Engineering (Cahners), August 1999, page 3.(“Browner stresses the panel did not challenge the science”)

Opdyke, Jeff D., Airline Seeks OK on Tool to Beat Fog, Alaska Airlines Seeks Wider Use of Navigational Aid”, Wall Street Journal Northwest, 1 September 1999.pg ?, NW4.

“United Plans Denver Push”, Aviation Week, 4 October 199, pg 47.

“Squabbles Persist over ATC delays”, Aviation Week, 4 October 1999. Pg 47.

Leschi News, Issue 161, May 1999.

Washington Air Quality Reports available at http://www.wa.gov/ecology/air/airhome.html

Foster, Heath, “Puget Sound area in risk of violating EPA Pollution Laws, Growing Smog means we could lose some US highway money”, Seattle Post-Intelligencer, 22 April 1999

Airline News, 16 June 1999 , Flight attendants with Alaska Airlines have reported air quality problems

“DC Has Higher Per-Capita Cancer Risk In Its Air Than Any of the 50 States, EPA Estimates Offer First-Ever Localized View Of Clean Air Act Health Protections” Environmental Defense Fund, 20 April 1999

Port of Seattle letter, from Barbara Hinkle, Health Safety & Environmental Management,, To Barbara Stuhring, dated 21 May 1996 (admits glycol not treated, ROD to include this letter)

Brown, A., To Expert Arbitration Board c/o Jerry Dinndorf, PSRC, 18 February 1996. (cold climate homes, R 7-35 admits models wrong)

Leonard, Edward C., Vinyl and Diene Monomers, Wiley-Interscience, A Division of John Wiley & Sons, New York 1971.

Gosselin, Robert, MD, Phd., Smith, Roger P, Phd, Hodge, Harold, PhD, D.Sc, Clinical Toxicology of Commercial Products, Williams & Wilkins, Baltimore, 1981.

“FAA Tests Infrared Deicers”, Aviation Week, 1 May 1995, pg 38.

Miller, Kay, “NASA, Honeywell test system to air airports with close parallel runways”, Star Tribune, 7 November 1999 (see Appendix K)

Kiernan, Bette, MFCC, Letter to J. Saporito regarding airlines, Flying off Course etc., 21 July 1998

“Sleeping Brain is Wary”, Newsday, pp A07. (John Hopkins University, Serena Gondel, Dr. Gregory Krauss, frontal lobe very active)

Munoz, Lorenza, “El Toro Foes Fin Allies Fighting Worldwide” Los Angeles Times, 4 July 1998. Pg 1 (mentions SeaTac) (file AB H1 207)

Public Notice of Port of Seattle, File 1996-4-02325, Public Notice Date 30 September 1999

Brown, A., Wetlands and Water Comments on Revised Public Notice of Port of Seattle File 1996-4-02325, Public Notice Date 30 September 1999, Rev A, 1 December 1999 Submitted to DOE (typographical corrections made to version sent to Army Corps of Engineers 29 November 1999)

“Aviation and the Environment: Aviation’s Effects on the Global Atmosphere Are Potentially Significant and Expected to Grow”,  Government Accounting Office Report RCED-00-57. 27 February 18, 2000. (available on line at www.gao.gov)

KIRO Interview, Port Commissioner Gina Marie Lindsey, 10 July 1999.

“Planes and Pollution”, (105N2 FOR: 172) Environmental Health Volume 105, Number 2, February 1997. (summarizes Flying Off Course), available at http://ehpnet1.niehs.nih.gov/docs/1997/105-2/forum.html#planes

”Breathing Easier” (104N10 FOR: 1024), Environmental Health Perspectives, Volume 104, Number 10, October 1996 available at http://ehpnet1.niehs.nih.gov/docs/1996/104-10/forum.html#breathing

Norris, Gary A, Timothy Larson, U of WA Dept of Civil Eng, Burdal, Sarah of DOE, “Atmospheric Observations of Nitrogen Dioxide in Seattle Wash” Doc No 94WP88.05 page 5. 1994

Occupational Exposure Limits for Airborne Toxic Substances: Values of Selected Countries, Third Edition,, Occupational Safety and Health Series No. 37, International Labour Office, Geneva, 1991

Furney, Al, “Fatal Traffic Accident – Haul Truck”, Accident  17 June 1998.

“Earthquake Hazards in the Pacific Northwest”, http://www.geophy.washington.edu?CREW/Other/hazmap.ntml, 22 March 1999

“Sea-Tac Mitigation Study”, Burien - Airport Assistance and Mitigation Studies, Hellmuth, Obata and Kassabaum (HOK) Final released ? March 1997

“Guidelines for Community Noise”, World Health Organisation 1999 (download from: http://www.who.int/peh/noise/noiseindex.html

“Urban noise a growing problem”, National Post, Tuesday, April 25, 2000
http://www.nationalpost.com/news.asp?s2=national&s3=toronto&f=000425/269605.html

“The sounds of silence are music to the ears of city noise activist”, National Post, Tuesday, April 25, 2000 http://www.nationalpost.com/news.asp?s2=national&s3=toronto&f=000425/269598.html

NoiseWatch, Toronto Canada http://www3.sympatico.ca/noise/- misc noise and health references

Williams, Carol J., “With the end of the cold war, Europe now faces wall of noise”, LA Times –Environment section, 27 March 1999. Available on Reading List link of Noise Watch at http://www3.sympatico.ca/noise/  -Alarming health and financial costs of noise {“An 11-year research project involving more than 1,000 heart patients found that noise, especially when it disrupts sleep, produces stress hormones that accelerate aging and heart disease, Ising says”}

“Report of the Urban Noise Task Force, City of Vancouver”, April 1997. Available on Reading List link of Noise Watch at http://www3.sympatico.ca/noise/

Deborah Sheiman Shprentz, Clean Air & Energy: Air Pollution: In Depth: Report, Breath-taking Premature Mortality Due to Particulate Air Pollution in 239 American Cities. May 1996. Mortality information available online at www.nrdc.org. Ranked Seattle 27 of 239 metropolitan areas for premature cardiopulmonary death due to PM10. (501 deaths per year, 31 per 100,000 year)

Toxic Chemicals: Long-Term Coordinated Strategy Needed to Measure Exposures in Humans GAO/HEHS-00-80, May 2, 2000 (PREPUBLISHED)*.

Aviation and the Environment: FAA’s Role in Major Airport Noise Programs. RCED-00-98. 69 pp. plus 10 appendices (32 pp.) April 28, 2000.   http://www.gao.gov/new.items/rc00098.pdf

Air Pollution: Status of Implementation and Issues of the Clean Air Act Amendments of 1990. RCED-00-72. 21 pp. plus 8 appendices (37 pp.) April 17, 2000.  http://www.gao.gov/new.items/rc00072.pdf

Public Health Impact of Large Airports - Sept. 1999: Report of the Health Council of Netherlands 194 page report dealing with air, noise, soil and water pollution near large airports.

Airports and Compatible Land Use, Volume 1, Washington State Department of Transportation, Aviation Division, revised February 1999.

Topographical maps with creeks shown - www.topozone.com

EPA Database with US Emissions of 33 toxic chemicals (maps of individual states too) at www.epa.gov/ttn/uatw/nata

State specific Lung Disease Data Feb 2000 (includes asthma) at www.lungusa.org/data

Site with misc reports. See CAW website http://www.us-caw.org/ such as for McCually, Frick & Gilman air pollution report, Burien HOK study and other useful reports

Site with misc reports. See ACC website http://www.ci.des-moines.wa.us/acc.html

Site with misc reports. See RCAA website http://www.rcaanews.org/, See their Library. Check out their links too.

Dumser, Brian PhD, CIH, Chair of the Subcommittee, Winthrop Community Health Survey, Winthrop Environmental Health Facts Subcommittee (Winthrop Airport Hazards Committee) Winthrop Board of Health, August 18, 1999 This study regarding Logan Airport in Boston, MA, USA is available under Studies at CAW site http://www.us-caw.org/

The Environmental Organisation, Copenhagen, “Emission report”, 2000. Available under Studies at CAW site http://www.us-caw.org/

Preliminary Study and Analysis of Toxic Air Pollutants from O’Hare International Airport and the Resulting Health Risks Created by these toxic emissions in surrounding residential communities”,  (Chicago Toxic Air Report ), City of Park Ridge, August 2000. available at http://www.areco.org/ (identifies health risks 32 miles from airport)

Clean Air & Energy: Transportation: In Depth: Report Exhausted by Diesel How America’s Dependence on Diesel Engines Threatens Our Health, National resource Defense Council at http://www.nrdc.org/air/transportation/ebd/ebdinx.asp (11-17-2000)

Holzman, David, Plane Pollution, Environmental Health Perspectives Volume 105, Number 12, December 1997 (available via links from www.areco.org/

World: Europe Chemical plane crash inquiry, BBC News, January 27, 1999 (photo of approx 10 story apartment cleaved by aircraft) at http://news.bbc.co.uk/hi/english/world/europe/newsid_263000/263813.stm

Hansen, Dennis, M.D. and Sanders, Lee A., M.D., Ph.D. The Adverse Health Impacts of Airport Expansion with Particular Reference to Sea-Tac International Airport. August 1992. (available on line through RCAA Library, www.rcaanews.org/ )

Urry, Doug (U of WA) , Larson, Timothy (U of WA) , Williamson, John, Frost, Jim and Knowlton, Doug, Sea-Tac Airport Spatial NO2 Study, WA State Dept of Ecology, (1998 data, draft)

Frost, Jim and Knowlton, Doug, Oxides of Nitrogen and Particulate Monitoring Study for the SeaTac Area 1998/1999, WA State Dept of Ecology, draft 13 December 1999.

Hileman, Bette, “Protecting a Child’s Health, Hearing examines steps government should take to study risks from toxic chemicals”, Chemical & Engineering News, 12 June 2000, page 31 (asthma epidemic)

Atlas of Cancer Mortality in the United states, 1950-94, The National Cancer Institute, (geographical patterns of US cancer deaths, order oublications.nci.nih.gov or phone US 800-422-6237)

Piazza, Bill, Los Angeles Unified School District, Environmental Health and Safety Branch for Santa Monica Working Group, “Santa Monica Municipal Airport, A report on the generation and downwind extent of emissions generated from aircraft and ground support operations”, June 1999. under studies at  www.us-caw.org/, accessed November 2000

Sidney, Australia Cancer maps, under studies at  www.us-caw.org/, accessed November 2000

US EPA Cumulative Exposure Project, Twin Cities (Minneapolis Minnesota) cancer maps, under Studies at www.us-caw.org/, accessed November 2000.

Meister, Edward, A, Donatelle, Rebecca J, The Impact of Commercial- Aircraft Noise on Human Health: A neighborhood Study in Metropolitan Minnesota, Environmental Health November 2000, page 9-15.

Brink, Susan, Sleepless Society: In staying up half the night, we may risk our health, U.S. News & World Report, 16 October 2000. Pages 63-72.

Smog May Induce Heart Attacks, Las Vegas Sun, Associated Press, 5 June 2000. 060500495.html [SmogHeartAttacksJune2000.doc]

Hogue, Cheryl, Clean Air Act Faces Off Against Disabilities Act, Chemical & Engineering News, 11 September 2000. Page 6.

Hogue, Cheryl, Particulates Linked to early Deaths, Chemical & Engineering News, 3 July 2000. Page 6-7.

“Addressing Community Health Concerns around SeaTac Airport Progress Report on the Work Plan Proposed in August 1998, response to question, “Is it possible to monitor jet engine exhaust emissions or to model their path using data on prevailing winds and takeoff patterns”, progress report 3, prepared by WA State Dept. of Public Health, March 2000.

Email Ann Glusker (Seattle-King County Dept. of Health) to Arlene Brown, update Asthma Hospitalizations 1997-1998 and 1992-1998 Trends, data dated October 2000.

Fax Ann Glusker (Seattle-King County Dept. of Health) to Arlene Brown, revised Table 5 of February 1999 report (Ref. 61) Appendix A. Added one zip code. Data dated 3 May 1999.

“Air quality conformity review for Sea-Tac Master Plan Update”, by
Envirometrics, prepared for Airport Communities Coalition, dated 5 June 1996

“Revised traffic analysis for air quality conformity review of Sea-Tac
Master Plan Update”, by SMITH Engineering & Management, prepared for
Airport Communities Coalition, dated 5 June 1996

Year 2001 FAA Website http://www.faa.gov/ats/asc/Pubs.html
Annual Aviation Capacity Enhancement Plans
Airport Capacity Enhancement Plans
Airport Capacity Enhancement Plan Updates
*Airport Capacity Enhancement Tactical Initiatives
Airport Capacity Enhancement Terminal Airspace Studies

Year 2001 FAA web site  http://www.faa.gov/ats/asc/menu.html
Publications, Software, Capacity Links, New Large Aircraft, What’s Here, Points of Contact

APO TERMINAL AREA FORECAST DETAIL REPORT, http://www.apo.data.faa.gov/faatafall.HTM, web access 4 February 2001 (file TAF.xls)

FAA CODAS database (delays, weather, operations, etc), www.apo.data.faa.gov, sweb access February 2001

Airport Activity Report-1999, Port of Seattle. Available on Port of Seattle web site (file posAR199.pdf)

The following references, 266 through 283 are in “Section 3 Annotated References” Feb2001of comments submitted to Army Corps of Engineers and Dept of Ecology 16 February 2001, third attempt Permit Application 1996-4-02325 related to Wetlands/Water/Shoreline

Wilson, Marshall, “New Plan Could Ease SFO Delays/Procedure could
change need for more runway”, San Francisco Chronicle, 2 February 2001.  http://www.sfgate.com/cgi-bin/article.cgi?file=/chronicle/archive/2001/02/02/MNW163624.DTL

Wilson, Marshall, “New Radar Approved To Reduce Delays at SFO /High-Tech system along with new flight path will allow more planes to land in bad weather”, San Francisco Chronicle, 9 February 2001.  http://www.sfgate.com/cgi-bin/article.cgi?file=/chronicle/archive/2001/02/09/MNW161233.DTL

Radar brings more flights”, Bay Area news briefs, 9 February 2001” $25 million radar ….to increase its bad-weather capacity from 30 arrivals per hour to as many as 37”

UPS Aviation Technologies to Build Next-Generation GPS Engine, press release 28 December 1999. Available on web February 2001 (www.upsat.com, pressrelease_waas_gps.html)

FAA Delay information shows SeaTac weather delays are related to the DESTINATION airport rather than SeaTac, downloaded 9 February 2001 http://www.fly.faa.gov/

Ridder, Knight /Tribune, Griffin, Greg , The Denver Post, February 08, 2001, “Denver Airport Ranks Among Top Five for Business Travel”

Hanchett, Doug, Satellite airports ease Logan’s load , Boston Herald, 26 January  2001.

ALONSO-ZALDIVAR, Ricardo,  “Runway Error Marred LAX Ceremony Aviation: Two 737s almost collided as airport officials gathered to receive a recent safety award.”, Los Angeles Times,  7 February 2001.

“Northwest Airlines to Acquire 52 New Aircraft”, PRNewswire, 16 January 2001.

Mathis, Jimmie, Boeing SPEEA (engineering) Union Council Highlights, 8 February 2001, Union endorsed legislation to limit federal money to runways large enough to “accommodate Boeing 737 and its derivatives”.

Aviation Watch Newsletter, “Did you know?” Remarks of NASA Administrator,  Daniel S. Goldin “The Future of Aerospace Transportation”   International Transportation Symposium held October 10, 2000, newsletter dated 27 January 2001

“Fuel spill contaminates neighborhood creek”, Channel 13-TV News Indianapolis, IN MSNBC, Extracted from Aviation Watch Newsletter dated 3 February 2001

“ANCIENT UNDERGROUND FRACTURES MAY THREATEN GROUND WATER SUPPLIES”, Columbus Ohio, 3 January 2001 (in email from B. Fish 4 Jan 2001)

“Radiant Energy’s InfraTek included in FAA advisory circular for design and
 performance standards for infrared deicing system”, Aviation Watch/PR Newswire, 3 October 2000.

Pilcher, James, “Airport OKs sound insulation 33 residences involved”,
The Cincinnati Enquirer, 16 January 2001 (another $535,000 added to about $125 million to date)

Worthington, Rogers Chicago Tribune Staff Writer. Freelance writer Dean Geroulis contributed to this report., “DATA SHOW HIGH O’HARE NOISE LEVELS IN WIDER AREA MORE TOWNS AFFECTED, SUBURBAN GROUP SAYS”, 19 January 19 2001.

“Quartermaster will receive Audubon designation”, email to Arlene Brown, dated 13 February 2001 regarding Maury Island

Bay Area airports on shaky ground - KTVU/Fox 2 - Jan 18, 2001. Aviation Watch

Finch, Bill, “Ozone hot spots can often be found in suburbs of major cities” Mobile Register, reprinted in Aviation Watch Digest Number 600, 14 November 2000.

Morgan, David, N.Y. Tops FAA List for Air Delays, ABC News, 31 January 2001. webabcnews.com, http://more.abcnews.go.coom/sections/us/dailynews/faaselays010131.html

Hoffman, Jonathan (Center for Advanced Aviation System Development, Mitre), Voss, William R (FAA AUA-1)., Analytical Identification of Airport and Airspace Capacity Constraints”,  3rd USA/Europe Air Traffic Management R&D Seminar Napoli, June 2000 (file name Hoffman4_ATM.pdf accessed on  web February 2001)

Power, Stephen (Staff reporter Wall Street Journal), “FAA Rule on Close-Flying Planes
Prompts Safety Board’s Criticism “ Business Fare, 9 February 2001 “The Transportation Department’s inspector general recently found that controller errors rose from 764 in 1996 to 1,154 in 2000. Although no collisions occurred, the inspector general has urged the FAA to address the problem

Kundu, Micheal, “Northwest Orca Populations Declining”, Sierra Club Cascade Crest Newsletter, January/February 2001, Volume 22, Issue 1,  pages 12-13.

Project Sea Wolf (northwest orcas), home.earthliink.net/~projseawolf

Santha, Lanke PE, Santhe, Calasta PhD, “Facts on Coir: Lessons Learned from the Past”, Rolanka International ,  http://www.rolanka.coom/art2.htm downloaded 3 January 2001

Tables of “Outlook/Specifications” Aviation Week, 15 January 2001

Port of Seattle Flight Tracks Hearing, Sea-Tac Airport, 18 May 2000.

Port of Seattle Flight Tracks Hearing, Highline Performing Arts Center, Fall 2000.

WA Dept of Ecology (DOE) Public Workshop on Highline Aquifer, Highline Performing Arts Center, Burien, WA, 14 September 2000.

Brown, Arlene, “Comments on the Sea-Tac Runway Fill Hydrological Studies Report dated 19 June 2000, To Dept. of Ecology Fitzsimmons, Tom, Garland, Dave, Hellwig, Ray  and Luster, Tom, copy to Army Corps of Engineers J. Freedman, 12 September 2000

SR509 Extension Public Meeting at Tyee High School, SeaTac WA 10 January 2001.

WA 57th Legislature, 2001 Regular Session HOUSE BILL 1237, By Representatives Keiser, Schual-Berke, Poulsen, McDermott, Santos, Mitchell and Miloscia, Read first time 01/22/2001.  Referred to Committee on Finance. AN ACT Relating to airport noise property tax exemptions for port district property taxes; amending RCW 84.55.010; adding a new section to chapter 47.68 RCW; and adding a new section to chapter 84.36 RCW. Olympia WA Hearing 1 February 2001.

NPDES Permit WA-002465-1 Public Comment Hearing on Modification, Burien Public Library, Burien WA, 12 February 2001.

WA 57th Legislature, 2001 Regular Session HOUSE BILL 1824, by Representative Shay Shual-Berke’s et al., House Agriculture and Ecology Committee hearing 13 February 2001.

AC 150/5300-14 Change 2, Design of Aircraft Deicing Facilities, dated 31 August 2000

AC 150/5370A Change 7, Standards for Specifying Construction of Airports, dated 29 January 1990

FAA Order 5054 4A, Airport Environmental Handbook , Chapter 10, “Tiering, Time Limitations, Written Reevaluations”, www.faa.gov/arp/app600/5054a/chap10.htm

“Changing Our Waterways, Trends in Washington’s Water Systems”, prepared by  Washington State Department of Natural Resources, 2000.

Article contained announcement on gate technology with North Terminal, Highline Times, 18 October 2000. (site down can’t confirm title)

Nichols, Ralph, “Highline Hospital begins asthma education project”, Highline Times, 26 November 2000.

Brown, Arlene, “Comments on Permit Application 1996-4-02325 related to Wetlands/Water/Shoreline”, To Army Corps of Engineers, Jonathan Freedman and Dept of Ecology (DOE), Ann Kenny, e-mailed 16 February 2001

Spicer ?, Chemical Composition and Photochemical Reactivity of Exhaust from Turbine Engines. 1994

ACC  401/404 permit comments submitted by experts December 1999, http://www.ci.des-moines.wa.us/acc.html

ACC  401/404 permit comments submitted by experts February 2001 http://www.rcaanews.org/401-40401acc.htm

Patrick C. Lucia, Ph.D.,P.E.,G.E. , Edward Kavazanjian, Jr., “ Comments on Seattle Tacoma International Airport Project  Third Runway – Embankment Fill and West MSE Wall, and  Industrial Wastewater System Lagoon #3 Expansion Project  On Second Public Notice, GeoSyntec Consultants, 16 February 2001 (for ACC) http://www.rcaanews.org/401_01geosys216.htm

EPA Air Quality Monitoring, Modeling and Related Data, 8 hour ozone data links for data by monitor, county and state  http://www.epa.gov/ttn/rto/areas/aqdata.htm, accessed April 2001

EPA, Washington’s ozone monitoring site map http://www.epa.gov/ttn/rto/areas/maps/wasite.gif,  web April 2001

EPA, tons of NOx by Washington County , http://www.epa.gov/ttn/rto/areas/state/cnty/wantot.gif  ,25 October 2000, accessed web April 2001

EPA Vehicle Miles Traveled (VMT) by State and County, http://www.epa.gov/ttn/rto/areas/vmt/stindex.htm, accessed April 2001

1999 Air Quality Trends Report , Washington Dept of Ecology,  http://www.ecy.wa.gov/programs/air/downloadable_air_quality_reports.htm, web March 2001

Comparative map of airport sizes including Sea-Tac http://www.portseattle.org/images/elements/seatac/airsizes2.gif, if above does not work go here http://www.portseattle.org/seatac/projects/need.htm and follow link from there, accessed April 2001

Daley, Beth, Globe Staff “Logan to levy pollution charges, Fees will help cut smog component”, Boston Globe,  7 April 2001, page 1. (AvWatch 4/7/01 also)

Scot Lehigh, Globe Staff, Peak-period pricing could help at Logan, Boston Globe, 6 April 2001, (AvWatch 4/6/01 also)

Matthew Brelis, Globe Staff, Massport pushing alternative airports to Logan, Boston Globe, 31 March 2001, (AvWatch 3/31/2001)

Gruner, Peter, “European Study Shows City Noise Leads to Serious Ill Health Effects”, Evening Standard , London England, page 18., 9 October 1998. available from Reports link of http://www3.sympatico.ca/noise/  (“Children living around Munich airport were monitored over three years and found to have quite pronounced changes in blood pressure.”

HEI publishes study on lung clearance of particles containing  benzo[a]pyrene - May 2001, Report 101 - Respiratory Epithelial Penetration and Clearance of Particle-Borne Benzo[a]pyrene.  http://www.healtheffects.org/news.htm

Update - HEI Quarterly Newsletter - Spring 2001,   HEI publishes study on rats exposed to Mexico City air - April 2001,  Report 100 - Respiratory Tract Toxicity in Rats  Exposed to Mexico City Air  http://www.healtheffects.org/news.htm

HEI publishes final version of National Morbidity, Mortality, and Air Pollution Study, Part II -  April 2001  Report 94 - National Morbidity, Mortality, and Air Pollution Study.  Part II: Morbidity and Mortality from Air Pollution in the United State. http://www.healtheffects.org/news.htm

Technology, Climate, and Health, The report of a joint Health Effects Institute/Heinz Center workshop on the Health Implications of   Technological Responses to Climate Change At the workshop, held November, 2000 in Washington DC and sponsored by the National Institute of Environmental Health Sciences, experts in technology and health assessed technologies likely to increase in use in  response to climate change, and began to identify both public health questions that might arise  about those technologies, and research needed to answer those questions. http://www.healtheffects.org/news.htm

WHO/HEI meeting on Particulate Air Pollution - March 2001 , A meeting “Understanding the Health Effects of Air Pollution: Recent Advances and Outstanding  Questions” held on March 6 and 7, 2001 in Brussels  http://www.healtheffects.org/news.htm

Health Effects Institute HEI Report 97    Mark S Goldberg, John C Bailar III, Richard T Burnett, Jeffrey R Brook, Robyn  Tamblyn, Yvette Bonvalot, Pierre Ernst, Kenneth M Flegel, Ravinder K Singh, and Marie-France Valois, Identifying Subgroups of the General Population That May Be Susceptible to Short-Term  Increases in Particulate Air Pollution: A Time-Series Study in Montreal, Quebec,  http://www.healtheffects.org/news.htm  PDF files (12/13/00)

AVIATION NOISE EFFECTS , FEDERAL AVIATION ADMINISTRATION,   WASHINGTON, DC, March 1985, U.S. DEPARTMENT OF COMMERCE, National Technical Information Service,  http://www.nonoise.org/library/ane/ane.htm

Victims of Indianapolis Expansion Library at http://members.iquest.net/~bsuleman/library.htm, May 2001

Holland, Walter, Professor,  Noise and Health, June 1997, http://www.hacan.org.uk/proofs/hac61.htm

Meecham, W.C. and Shaw, N.A., “Increase in Mortality Rates Due to Aircraft Noise,” Proc. of Inter-Noise 93, Leuven, Belgium, (Reviewed Paper), pp. 1091-1094, 1993. http://www.mae.ucla.edu/academic/faculty/meecham.htm

The effect of night time airplane noise on excretion of stress hormones in residents living near airports. Maschke-C; Arndt-D; Ising-H; Laude-G; Thierfelder-W; Contzen-S. Schriftenr-Ver-Wasser-Boden-Lufthyg. 1995; 96: 1-140, I-XIX

Docteur Pierre de Marneffe, “Répercussions des vols de nuit sur la qualité de vie et la santé des riverains d’aéroport” , November 1997, great list of noise/health references http://www.net-sky.be/demarnef.htm (accessed May 2001)

Acceleration of Lupus Erythematosus-Like Processes by Low Frequency Noise in the Hybrid NZB/W Mouse Model, Águas AP, Esaguy N, Grande NR, Castro AP, Castelo Branco NAA Aviat Space Environ Med 1999; 70(3, Suppl.):A132-6 (Exposure of lupus-prone mice to low frequency noise accelerates the expression of the autoimmune disease and it affects the immune system by raising the number of splenic IgM+ B lymphocytes and CD8+ T cells.) http://www.asma.org/abstracts/v70n3s/0132.html

“Team probes Atlanta heat island” , Environmental News Network,  24March 1999, http://www.enn.com/news/enn-stories/1999/03/032499/heatisland_2295.asp

Dale A. Quattrochi (dale.quattrochi@msfc.nasa.gov), NASA, Global Hydrology and Climate Center, Huntsville, AL , Jeffrey C. Luvall (jeff.luvall@msfc.nasa.gov) , NASA, Global Hydrology and Climate Center, Huntsville, AL, ‘High Spatial Resolution Airborne Multispectral Thermal Infrared Data to Support Analysis and Modeling Tasks in EOS IDS Project ATLANTA’,  http://wwwghcc.msfc.nasa.gov/atlanta/. Last updated 8 July 1997

“Some Countries Use MANY Methods To Study Aircraft Noise Impacts:”, Aviation Conspiracy Newsletter #129, August 19, 2001 (fantastic color phots of 70dB noise at http://pages.prodigy.net/rockaway/newsletter129.htm

Peter Corbett and Tom Zoellner , “Risky aviation? Experts differ” , The Arizona Republic online , 14 July 2001,

Aviation experts say chances are slim that a plane would crash into a planned Arizona Cardinals football stadium, just east of Sky Harbor International Airport. But some pilots think it is foolish to even take the risk.  //www.arizonarepublic.com/special07/articles/0714stadiumside14.html

Shaun McKinnon and Paul Matthews , “FAA will declare stadium a hazard”, The Arizona Republic online , 14 July 2001, The Federal Aviation Administration is prepared to declare the new Cardinals football stadium a safety hazard, a conclusion that could undermine the project at its current location. Full story at http://www.arizonarepublic.com/special07/articles/0714stadium14.html

Department of Ecology August 10, 2001 401 Certification    (second issue, first was withdrawn) http://www.ecy.wa.gov/programs/sea/SeaTac3rdRunway.pdf

Washington EPA Air Data database site  http://www.epa.gov/air/data/monsum.html (use to access King County  lead and 4 ozone exceedences for 1998 etc)

USGS topographic map from the TopoZone! zoom in and out to see the area. Red cross mark above radio tower is location of third runway, near the great wall. http://www.topozone.com/map.asp?z=10&n=5255768&e=551475&s, corresponds to latitude  47.4427º, longitude -122.3212º, Map center is UTM 10 551179E 5254365N , DES MOINES quad

Aerial photos, http://terraserver.homeadvisor.msn.com. Search for Seattle-Tacoma International Airport or try this link http://terraserver.homeadvisor.msn.com/image.asp?S=13&T=1&X=345&Y=3284&Z=10&W=2

Great Wall of Sea-Tac Figure at http://www.geocities.com/bzdiving/GreatWallofSeaTac.html. Link from web site: Miller Creek, a place of history, peace and change...  http://www.geocities.com/bzdiving/

McKinnon, Shaun, “Jets would be low, loud over new stadium”
 The Arizona Republic, Arizona Republic, 29 July  2001 (Avwatch 27 September 2001)

For the decision of the European Court of Human Rights, see the press
release re. Hatton & others v United Kingdom, published 2nd October, at
www.echr.coe.int. The full judgment can also be found at the court¹s website
(under OJudgments¹) or < more quickly < at the website of the solicitor
representing the residents: www.richardbuxton.co.uk.  (application number
36022/97, ban Heathrow flights between the hours of 11pm and 7 am.)

Do Environmental Pollutants Make Cancers More Aggressive?
Copyright © 2001, Medical College of Wisconsin. , October 19, 2001 AvWatch

Radiant Energy Corporation announces American Airlines approval to use
InfraTek to deice aircraft, PRNewswire  reprinted in October 19, 2001 AvWatch

A NIRS project contains all of the input files, output files, reports, and graphics necessary to complete the noise analysis.
 http://www.faa.gov/ats/ata/ata300/Nirs_site/nirs_overview/index.html

Toxic air meeting, WA Dept of Health, Seattle-King County Dept of Health, Dept of Ecology, EPA, Port of Seattle, Clean Air Agency, Community Health Representatives (Arlene Brown, Dr Topiwala, Audrey Richter), Rep Shay-Burke, Held Highline Hospital, Burien WA, December 2001

Revised Draft Environmental Impact Statement and Draft 4F Evaluation, SR-509: Corridor Completion/I-5/South Access Road, January 2002.  (accessed March 2002) http://www.wsdot.wa.gov/regions/northwest/SouthKing/projects/sr509/documents/01_Front_Matter.pdf

SR 509 Extension Public Hearing, Highline Community College, 25 February 2002 (Arlene Brown submitted written comments in addition to oral comments)

Toxic sediment meeting (ASARCO), Seattle-King County Dept of Health, Dept of Ecology, Community Health Representatives (Arlene Brown, Audrey Richter), Burien Deputy Mayor Rose Clark, Held Burien City Hall, Burien WA, 21 March 2002

FAA Airport Advisory Circulars http://www.faa.gov/arp/150acs.htm

FAA Advisory Circular Airport Design AC150/ 5300-13, Appendix 8, Runway Design Rationale, http://www.faa.gov/arp/pdf/5300-132.pdf (mandatory for Federal funds eligibility)

FAA Advisory Circular Airport Design AC150/ 5300-13, Change 4, Table 2-4 Figure 2-3 and Figure 2-4 Runway Protection Zone (RPZ) dimensions and sketch http://www.faa.gov/arp/pdf/5300-131.pdf , Tables 3-1, 3-2, 3-3 and Fig 2-3 for Object Free Area (OFA)

Seattle-King County Dept of Public Health Public Health News Release “Public Health issues report citing alarming increase in unhealthy body weight” (King County adults are 11 pounds heavier than 15 years ago), 15 March 2002 http://www.metrokc.gov/health/news/02031501.htm